## Slide 1: Further samples…
Peter Willendrup
Slides adapted from Mads Bertelsen, ESS DMSC
Slides adapted from Mads Bertelsen, ESS DMSC

## Slide 2: Further samples in McStas
Models for SANS and reflectometry
Inelastic scattering, examples:
    Phonon_simple
    Isotropic_sqw
McStas performance, TAS / Chopper

## Slide 3
Small angle scattering SANS
SANS method can be used for many types of material
Often: Molecule + Liquid (buffer solution)
Isotropic scattering

## Slide 4
SANS
Small Angle Neutron Scattering
Elastic Scattering
Small angle -> small q -> big r
Gain information on the molecular scale 10-100Å
Low signal to noise
Contrast method
Instrument requirements: good collimation, long flight distance after detector.

## Slide 5
SANS other samples
SANS_AnySamp.comp
SANS_DebyeS.comp
SANSCylinders.comp
SANSEllipticCylinders.comp
SANSGuinier.comp
SANSLiposomes.comp
SANSNanodiscs.comp
SANSNanodiscsFast.comp
SANSNanodiscsWithTags.
SANSNanodiscsWithTagsFast
SANSPDB.comp
SANSPDBFAST.comp
SANSShells.comp
SANSSpheres.comp
McStas has a suite of SANS-models:
Try ellipsoidal and
cylindrical particles
-or-
Elliptic cylinders
Go for Nanodiscs and Liposomes
Also – SASmodels from SASview

## Slide 6
SANS spheres
Dilute, monodisperse, hard spheres in solution, with given contrast and radius

## Slide 7
SasView_models

## Slide 8
SasView_models

## Slide 9: Inelastic scattering S(q,w)
partial differential cross section
Scattering function
Phonons, Spin waves, …

## Slide 10: Popular component: Phonon_simple
One isotropic acoustic phonon branch in all Brillouin zones on FCC Bravais single crystal
M - Atomic mass
b – scattering length
n – bose factor
a – fcc lattice spacing
c - speed of sound
𝜿 – measured q vector
q – Phonon scattering vector
For FCC Bravis
Dispersion

## Slide 11: Popular component: Phonon_simple
Dispersion relation, theory and mcstas
q
⍵
q0

## Slide 12: Popular component: Phonon_simple
Example of the output
4 meV energy transfer

## Slide 13: Popular component: Isotropic_sqw
Isotropic processes (powder, liquid, …)
Use data files to describe S(q,w) directly, coherent and incoherent
Supports concentric

## Slide 14: Popular component: Isotropic_sqw
Isotropic processes (powder, liquid, …)
Use data files to describe S(q,w) directly, coherent and incoherent
Supports concentric
q
q
⍵
P(⍵)
P(Q|⍵)

## Slide 15: Popular component: Isotropic_sqw
Rb liquid in time of flight
Coherent and incoherent

## Slide 16: Inelastic scattering in McStas
Monte carlo sampling issues
Need to sum over large amount of possible final states to find cross section
Need large amount of rays to sample all the options
qz
qx
qy
+⍵
dqy
dqx
dqz
+d⍵

## Slide 17: TAS
Only a small fraction of neutrons arrive, most are simulated in vain

## Slide 18: Chopper spectrometers
Only a small fraction of neutrons arrive, most are simulated in vain

## Slide 19: Conclusion
Inelastic scattering supported in McStas, but could use more sample components
Longer computational times required
Advantages from simulation especially important for spectroscopy (resolution function)