## Slide 1: Inelastic samples
Mads Bertelsen, ESS DMSC

## Slide 2: Inelastic scattering in McStas
Introduction to inelastic scattering
Included components
    Phonon_simple
    Isotropic_sqw
Sampling performnace with data approach
McStas performance, TAS / Chopper
Exercise

## Slide 3: Inelastic scattering S(q,w)
partial differential cross section
Scattering function
Phonons, Spin waves, …

## Slide 4: Popular component: Phonon_simple
One isotropic acustic phonon branch in all Briullion zones on FCC bravis single crystal
M - Atomic mass
b – scattering length
n – bose factor
a – fcc lattice spacing
c - speed of sound
𝜿 – measured q vector
q – Phonon scattering vector
For FCC Bravis
Dispersion

## Slide 5: Popular component: Phonon_simple
q
⍵
q0
Dispersion relation, theory and mcstas

## Slide 6: Popular component: Phonon_simple
Example of the output
4 meV energy transfer

## Slide 7: Popular component: Isotropic_sqw
Isotropic processes (powder, liquid, …)
Use data files to describe S(q,w) directly, coherent and incoherent
Supports concentric

## Slide 8: Popular component: Isotropic_sqw
Isotropic processes (powder, liquid, …)
Use data files to describe S(q,w) directly, coherent and incoherent
Supports concentric
q
q
⍵
P(⍵)
P(Q|⍵)

## Slide 9: Popular component: Isotropic_sqw
Rb liquid in time of flight
Coherent and incoherent

## Slide 10: Inelastic scattering in McStas
Monte carlo sampling issues
Need to sum over large amount of possible final states to find cross section
Need large amount of rays to sample all the options
qz
qx
qy
+⍵
dqy
dqx
dqz
+d⍵

## Slide 11: TAS
Only a small fraction of neutrons arrive, most are simulated in vain

## Slide 12: Chopper spectrometers
Only a small fraction of neutrons arrive, most are simulated in vain

## Slide 13: Conclusion
Inelastic scattering supported in McStas, but could use more sample components
Longer computational times required
Advantages from simulation especially important for spectroscopy (resolution function)

## Slide 14: Exercise
Use provided TAS instrument to scan the phonon dispersion
Requires that you work in folder containing components from the zip file
Futrher explanation on github