## Slide 1
McXtrace components and instruments
Peter Willendrup (pkwi@fysik.dtu.dk)

## Slide 2: In the big picture, McXtrace is this…

## Slide 3: In the big picture, McXtrace is this…
Instrument
The instrument defines our “lab coordinate system”

## Slide 4: In the big picture, McXtrace is this…
Component
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument
Instrument
Component
Component

## Slide 5: In the big picture, McXtrace is this…
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument - they have different function
Sample
Source
Monitor
Instrument

## Slide 6: In the big picture, McXtrace is this…
X-rays
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument - they have different function
X-ray photons particles are passed on from one component to the next, changing state under way
Sample
Source
Monitor
Instrument

## Slide 7: Placing components - source
One of the first components in your instrument is typically a source, which has a coordinate system like this….
z is along neutron beam direction
y is vertical
x at an angle of 90° wrt. z,y
x
y
z
Right-handed
coordinate system

## Slide 8: Placing components - source
Often the source coordinate system coincides with the “lab” coordinate system, denoted ABSOLUTE in McXtrace language, i.e.
COMPONENT Source = Source_flat(…) AT (0,0,0) ABSOLUTE
x
y
z

## Slide 9: Placing further components - RELATIVE
Placing further components is done by order of 1. Location, i.e
COMPONENT Source = Source_flat(…) AT (0,0,0) ABSOLUTE
x
y
z
x´
y´
z’
COMPONENT Capillary = Capillary(…) AT (0,0,1) RELATIVE Source

## Slide 10: Placing further components - RELATIVE
Placing further components is done by order of 2. Rotation, i.e
COMPONENT Source = Source_flat(…) AT (0,0,0) ABSOLUTE
x
y
z
x´
y´
z’
x”
z”
COMPONENT Capillary = Capillary(…) AT (0,0,1) RELATIVE Source
ROTATED (0,0.1,0) RELATIVE Source
(Reference labels can also be PREVIOUS or PREVIOUS+1 etc.)

## Slide 11: Components often have their origin at the centre of mass, i.e. for samples … but not for e.g. Capillary
Placing further components is done by order of 2. Rotation, i.e
COMPONENT Sample = Some_sample(…) AT (0,0,0) [RELATIVE] ABSOLUTE
x´
y´
z’
x
y
z
Generally speaking, the component author can choose
the meaningful coordinate system for the given problem!
- The McXtrace system takes care of the transformation between them….

## Slide 12: Component geometries are typically simple objects… But some have polygon-description of the surface
2D
3D

## Slide 13: Component classes
Sources - these define MC starting conditions / “inject” rays to our simulation
Optics - used to tailor properties of the X-ray beam
  Examples are mirrors, capillaries, lenses, zone-plates, choppers, collimators, slits, …
Samples - “matter” of some form
  Powders, single crystals, liquids, micelles in solution, reflecting surfaces…
Monitors - may probe the state of the X-ray beam and store histograms / event lists
Misc, obsolete
  “Other stuff” and “Old stuff”

## Slide 14: Component classes
Sources - these define MC starting conditions / “inject” neutrons to our simulation
Optics - used to tailor properties of the X-ray beam
  Examples are mirrors, capillaries, lenses, zone-plates, choppers, collimators, slits, …
Samples - “matter” of some form
  Powders, single crystals, liquids, micelles in solution, reflecting surfaces…
Monitors - may probe the state of the X-ray beam and store histograms / event lists
Misc, obsolete
  “Other stuff” and “Old stuff”
Common to all components:
They set, manipulate/interact with
or measure the state of the X-ray (ray)

## Slide 15: Sources, e.g. rotating anode
To first order emit uniformly into steradian

## Slide 16: Sources, e.g. rotating anode
Generally we are intersted in sending the input to an aperture, characterised by a certain solid angle , often corresponding to a rectangle x at a distance from the source
To first order emit uniformly into steradian

## Slide 17: Sources, e.g. rotating anode
The emmission intensity into our chosen solid angle can be a function of wavelength, time (pulsed sources) and possibly point of origin on the source surface (e.g. for partially coherent descriptions).
The emission of particles into the solid angle is in fact an integration and leads to a simulated “intensity” of .
In McXtrace, that integrated intensity is partitioned over a given set of particle rays referred to as ncount, -n or --ncount
The default ncount is 1e6 rays

## Slide 18: Sources, e.g. rotating anode
Our rays are emitted randomly, sampling and all variables of the source “spectrum”, i.e. wavelength, time and area
assigning ray weights such that

## Slide 19: X-ray (rays) in McXtrace - what are they?
The starting point on the surface, i.e. (in the code variables x,y,z)
The direction into and our / k (in the code variables kx,ky,kz)
The starting time (in the code the variable t)
The initial intensity / weight of the neutron ray (in the code the variable p)
If needed the initial
  Electric field polarisation (in the code the variables Ex,Ey,Ez)
  X-ray phase (in the code the variable phi)
Defining the ray starting conditions imply setting:
X-ray package:
Weight (p), # photons (left) in the package
Coordinates (x,y,z)
Wavevector (kx,ky,kz)
Polarization (Ex,Ey,Ez)
Phase ()
Time(t)

## Slide 20: X-ray / matter interaction 1: reflecting surface
1 starting situation
X-ray (ray)
Mirror surface
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
0

## Slide 21: X-ray / matter interaction 1: reflecting surface
2. Propagate to the mirror surface
X-ray (ray)
Mirror surface
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
0
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
1

## Slide 22: X-ray / matter interaction 1: reflecting surface
3. Checks (are we on surface, what is probability of reflection etc.)
X-ray (ray)
Mirror surface
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
0
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
1

## Slide 23: X-ray / matter interaction 1: reflecting surface
4. Reflect
X-ray (ray)
Mirror surface
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
0
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
1
(x,y,z,kx,ky,kz,t,Ex,Ey,Ez,phi,p)
2
Weight of final ray is adjusted according to reflectivity, see next slide

## Slide 24: X-ray / matter interaction in general
A photon hitting a sample can be:
absorbed, transmitted, or scattered

## Slide 25: X-ray / matter interaction in general
For a non-thin sample the probabilities for absorption, transmission or scattering are given by
t = sample thickness
microscopic cross section [barn/fm2]
number density [atoms/cm3]
macroscopic cross section [cm-1]
Samples

## Slide 26
Samples/Matter interaction in General in McXtrace
A photon ray hitting a sample can be:
transmitted+absorption, or scattered+absorption

## Slide 27: Transport of weight through the instrument…
Sample
Source
Monitor
Instrument
The weight multiplier of the j’th component, , is calculated by the probability rule where Pb is the physical probability for the event ”b“, and is the probability that the Monte Carlo simulation selects this event.
In case of “branching”, i.e. multiple outcomes, it is clear that
In a given component, the neutron intensity is adjusted by a multiplicative factor (probability)

## Slide 28: To first order, McXtrace is linear and follows sequence of components in your file…
1
1
2
2
3
3
Starting at the source

## Slide 29: To first order, McXtrace is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to first comp in the list

## Slide 30: To first order, McXtrace is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_xray=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.

## Slide 31: To first order, McXtrace is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_xray=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.
The order of components is important,
and in general overlaps should be avoided!