McStas: Liquids and Powders Dynamics
E. Farhi, ILL

---
Isotropic density samples in McStas
Outline
Scattering law, a bit of theory
The Isotropic_Sqw component and input data files
How to get S(q,w) data sets:
From MD
From lattice dynamics
From experiments
Exercise: a “liquid” TOF spectrometer
Exercise: separate contributions
Disclaimer: in case of errors and uncertainties, please correct me...

---
Neutron-matter interaction
Selections rules
Kf=Ki+Q
Ef=Ei+w
Bragg's law (diffraction on structure – atoms separated by distance d)
n%lambda = 2 %pi/K_i = 2 d sin %theta
Scattering law (intensity per solid angle and energy, dynamics)
{d^2 %sigma} over {d%OMEGA dE_f} = K_f over K_i [ %sigma over {4%pi} S(Q,%omega) ]
Holy Book (Squires)
Dynamical structure factor S(Q,w) is characteristic of each material
Reflects ordering of matter (atom/molecule positions – movements - domains)
Ki, Ei
Kf, Ei
Q, w
(d=2p/Q)
Material
2q

---
Scattering law
The double differential scattering cross section gives the probability for a neutron to scatter for a given solid angle and energy
The total intensity is the full integral over all scattering possibilities.
Effective total scattering cross section
 V.F. Sears. Adv. Phys., 24, 1, 1975.

---
Computing the total scattering probability
The total scattering cross section is given in (W,Ef) space, but S is given in (q,w)
A variable change must be done for the integration (Jacobian).
We like to play games
in (q,w) space
Effective cross section
in (q,w) space
n
p=func e^{-%rho hat %sigma x}
Probability to transmit
Scattering distribution
S(q,w)
with importance sampling to
scatter preferably where S is large

---
How to get S(q,w) data sets
Liq/Powder/Xtal
S(Q) or F(Q)
or S(|Q|,w)
Inter-atomic
potential u(r)
MDANSE
{ vec {F}}= - nabla u ({vec r}) = -m { vec %gamma }
McStas
Sqw
R, v
S(|Q|,w)
Pseudo-potential
Simulated
experiment
S(Q,w) 4D
MD step is done prior to the virtual experiment (NAMD, VASP, GROMACS, ...).
Computationally intensive (e.g. use clusters). Then use FFT(r,t)
McStas provides a few sample S(Q,w): Rb, Ge, H2O, D2O, D2, ...
Isotropic_Sqw: Handles elastic and inelastic for both coherent and incoherent channels
Experiments
(corrected)
Molecular
Dynamics
Ab-initio MD
Ab-initio Lattice Dyn.

---
Isotropic_Sqw syntax
Isotropic_Sqw(
  1. Sqw_coh=FILE_COH,
  2. Sqw_inc=FILE_INC,
  3. radius=R,
  4. height=H)
- More component parameters can specify geometry, physical properties, ...
- The data files specify the S(Q,w) or S(Q) values as a matrix with Q,w extent. Additional fields can be included as meta data (# lines).

---
Isotropic_Sqw data format
- Open McStas, select Help / Comp Ref, then Data files. Select a .sqw file, e.g. He4_liq_coh.sqw
- Look at format: Header and meta data, axes, matrix
- Used # fields:
  - density, weight, sigma, Temperature
- Meta data can be given as component parameters.

---
Isotropic_Sqw data format
# Sqw data file for Isotropic_Sqw
# liquid He4: coherent part, no incoherent, atomic number 2
# Elementary Excitation Data by R.J. Donnelly et al., J. Low Temp. Phys., 44 (1981) 471
# WARNING: line width is constant, intensity is not right
#
# Physical parameters:
# V_rho 0.072 atom density per Angs^3
# weight 4.002 in [g/mol]
# density 0.4784 in [g/cm^3]
# sigma_abs 0.00747 absorption scattering cross section in [barn]
# sigma_coh 1.34 coherent scattering cross section in [barn]
# sigma_inc 0 incoherent scattering cross section in [barn]
# Temperature 2 in [K]
# classical 0 experimental, contains Bose factor
#
# q axis values
# vector of m values in Angstroem-1
0.001000 0.011000 0.02 …
# w axis values
# vector of n values in meV
0.001391 0.011391 0.021391 0.0313 …
# sqw values (one line per q axis value)
# matrix of S(q,w) values (m rows x n values), one line per q value
9.721422 10.599145 11.344954 …
He4_liq_coh.sqw
Such files can be written from an iFit iData_Sqw2D object:
sqw2d = iData_Sqw2D(...);
saveas(sqw2d, ‘filename.sqw’,’mcstas’)

---
Sqw file from experiments
- Reduce the experimental data, correct it for e.g. empty cell, parallax, detector efficiency, …
- Correct for absorption, incoherent scattering, multiple-scattering, ...
- Integrate over |Q| as Isotropic_Sqw is isotropic.
- Write a text file with [Q,w] and S(Q,w) vectors/matrices. Add meta-data.

---
Sqw file from MD
- Set the system box, (pseudo) potential/FF
- Equilibrate, and couple to thermostat (NVT)
- Run calculator in MD mode (NVE)
- Convert trajectory (R,t) into S(|Q|,w) [MDANSE]
  - Analysis/Scattering/DCSF and DISF → .nc file
- Export into .sqw text files.
  - sqw2d = iData_Sqw2D(‘DCSF.nc’);
  - saveas(sqw2d, ‘DCSF.sqw’,’mcstas’);

---
Sqw file from Lattice Dynamics
- Create a crystal, calculate displacements or so.
- Assemble the ‘phonon’ representation
- Evaluate S(Q,w) on powder average
- Export to McStas Sqw

---
Sqw: Exercise 1: a liquid TOF
Aim: A simple spectrometer (and diffractometer)
- Create a new instrument from 'template (test)'.
- Call it Liquid_simple and define input parameters (lambda=2.36, string coh=”Rb_liq_coh.sqw”, string inc=”Rb_liq_inc.sqw”)
- Insert a Source_simple f1cm sending l=lambda with dl/l=1%. Focus onto a 1x1cm2 area.
- Insert an Isotropic_Sqw 3m away, using scoh=coh, sinc=inc with f1cm x 5cm.

---
Sqw: Exercise 1: a liquid TOF
- Add a Monitor_nD cylindrical detector f1m x 30cm, sensitive to (q,y) for diffraction, centred on the sample, with 100 bins.
- Add the same, but sensitive to (angle,energy) with automatic energy limits.
- Save, run in Trace 3D to check geometry.

---
Sqw: Exercise 1: a liquid TOF
- Run in Simulation/PGPLOT mode with 1e8 neutron events.
- Plot results !
- Comment on the diffraction pattern and the inelastic one.

---
Sqw: Exercise 2: contributions
Insert an instrument variable in the DECLARE block, as 'flag_scat'.
DECLARE %{
int flag_scat=0;
%}
After the AT token of the 'sample', insert an EXTEND block that sets flag_scat to the number of SCATTERED events.
EXTEND %{
flag_scat=SCATTERED; // nb of scattered events
%}

---
Sqw: Exercise 2: contributions
Duplicate the 2 monitors, and make them sensitive to multiple-scattering only. Add a WHEN(flag_scat) between the COMPONENT and the AT keywords:
COMPONENT …
WHEN(flag_scat > 1)
AT ...
- Save and Run !
- How much multiple scattering ratio at l=2.36 Å
- Make the sample f5cm and repeat.

---
Sqw: Exercise 3: from iFit: build
- McStas can be controlled from within iFit.
- Open Matlab/iFit
- Create the Liquid_simple model with:
  - model = mccode(‘Liquid_simple’)
- Plot the geometry with:
  - plot(model)	% has contextual menus
- Then run it with (default 1e6 event and pars)
  - data = iData(model, [], nan);
  - subplot(model)

---
Sqw: Exercise 3: from iFit: eval
- Specify parameters
  - data = iData(model, ‘lambda=2.36; coh=Cu.laz’)
- Do a scan:
  - data = iData(model, ‘lambda=[1.2 2.4 3.6]’)
- Change neutron events #
  - model.UserData.options.ncount = 1e7;

---
Sqw: Exercise 3: from iFit: optim
- Fix all parameters but lambda, Maximize model value:
  - mlock(model, ‘all’); munlock(model, ‘lambda’)
  - xlim(model, ‘lambda’, [1 3]); % bounds
  - fmax(model, ‘lambda=2.36’, ‘’, nan)
  - fmax(model, ‘lambda=2.36’, ‘OutputFcn=fminplot’, nan)

---
Sqw: Exercise 3: from iFit: crazy
- You can add two McStas models:
  - model=mccode(‘instr1’)+mccode(‘instr2’)
- Edit the instrument and re-compile
  - edit(model)
- ...