## Slide 1: McStas diagnostics
Mads Bertelsen, European Spallation Source, DMSC

## Slide 2: Overview
Monitors
Flags: EXTEND and WHEN combination
Monitor_nD and Pre_monitor_nD
    Correlations ”backwards” in instrument
Scatter_logger
    Overview of scattering

## Slide 3: Using monitors everywhere
In real experiments, we only measure the neutron once
In McStas you can add monitors along your instrument to understand how the beam changes
A bit obvious after a week of training

## Slide 4: Viewing a subset of data with EXTEND and WHEN
Flexible approach
May need to understand the code of the sample component
Can split the output into signal and background
DECLARE %{ int number_of_scattering; %}
TRACE
COMPONENT sample = Isotropic_sqw (…) AT (0,0,0) RELATIVE Sample_position EXTEND %{ number_of_scattering = SCATTERED; %}
COMPONENT psd_first_order = PSD_monitor (…) WHEN (number_of_scattering == 1) AT (0,0,0) RELATIVE Detector_position
COMPONENT psd_multiple_scat = PSD_monitor (…) WHEN (number_of_scattering > 1) AT (0,0,0) RELATIVE Detector_position

## Slide 5: Viewing a subset of data with EXTEND and WHEN
Flexible approach
May need to understand the code of the sample component
Can split the output into signal and background

## Slide 6: PreMonitor_nD and Monitor_nD
Use Monitor_nD to find correlations
PreMonitor_nD sends neutron state
Monitor_nD recieve state with the ”use premonitor” option
TRACE
COMPONENT PreMonitor_nD ( monitor_comp=At_moderator_position) AT (0,0,0.1) RELATIVE Source
COMPONENT guide = Guide_gravity(l=9.5,…) AT (0,0,2) RELATIVE Source
COMPONENT At_moderator_position = Monitor_nD( xwidth=0.12,yheight=0.12, options=”x bins=100, y bins=100, use premonitor”) AT (0,0,10) RELATIVE guide

## Slide 7: Examples of PreMonitor_nD results
PreMonitor_nD just after moderator
Monitor_nD at sample position
guide
monochromator
source
sample
Moderator origin of rays that go to the sample

## Slide 8: Scatter logger
Components used for logging what happens during McStas simulation
Use provided examples for use!
Scatter_logger
Scatter_logger_stop
Scatter_log_iterator
Scatter_log_iterator_stop
Source
Scatter_logger
guide
Scatter_log_iterator
Monitor_nD
Monitor_nD
Scatter_log_iterator_stop
Arm
Arm
Scatter_logger_stop
JUMP

## Slide 9: Scatter logger examples
Intensity loss along straight guide
Shielding thickness
Background
Test_Scatter_log_losses.instr

## Slide 10: Scatter logger examples
Intensity loss along straight guide
Shielding thickness
Background
Test_Scatter_log_losses.instr

## Slide 11: Scatter logger examples
Intensity loss along straight guide
Shielding thickness
Background
Test_Scatter_log_losses.instr

## Slide 12: Scatter logger examples
m value required for reflection
10 m straight guide with m=3
Test_Scatter_log_mvalues.instr

## Slide 13: Scatter logger examples
m value required for reflection
10 m straight guide with m=3
Test_Scatter_log_mvalues.instr
Reflection number 1

## Slide 14: Scatter logger examples
m value required for reflection
10 m straight guide with m=3
Test_Scatter_log_mvalues.instr
Reflection number 2

## Slide 15: Scatter logger examples
m value required for reflection
10 m straight guide with m=3
Test_Scatter_log_mvalues.instr
Reflection number 3

## Slide 16: Scatter logger examples
m value required for reflection
10 m straight guide with m=3
Test_Scatter_log_mvalues.instr
Reflection number 4

## Slide 17: Scatter logger examples
m value required for reflection
50 m elliptical guide with m=3

## Slide 18: Scatter logger examples
m value required for reflection
50 m elliptical guide with m=3
Reflection number 1

## Slide 19: Scatter logger examples
m value required for reflection
50 m elliptical guide with m=3
Reflection number 2

## Slide 20: Scatter logger examples
m value required for reflection
50 m elliptical guide with m=3
Reflection number 3

## Slide 21: Scatter logger examples
m value required for reflection
50 m elliptical guide with m=3
Reflection number 4

## Slide 22: m values for straight and elliptic
10 m straight guide
50 m elliptic guide

## Slide 23: Conclusion
The main advantage of simulation is that they further our understanding
Use diagnostics tools such as Scatter_logger and Monitor_nD to record information
Use this information to make better and cheaper instruments