Powder diffractometer
Use ESS_moderator_long.comp
Size = 0.02m, focus 0.02x0.02m at 149.9 m
pulse length d = 2.0 ms
repetition frequency f = 1/T=20 Hz
Standard thermal source (temp=325K)
Appropriate thermal wavelength
Otherwise default parameters
Place 3 TOF_monitors of the same size as the moderator
Directly after the moderator
At 6 m
At 149.9 m
Ex 1.1 : Adjust the timelimits to see the full pulse

---
Ex 1.2: Place TOFLambda_monitors instead of the TOF_monitors.
Notice the wavelength spread pr timechannel decrases with
distance from the moderator
Ex 1.3: Confirm that the integrated intensity is the same using settings
d=2.86 ms
f=14 Hz

---
Ex 2.1: Go back to the setting with d=2ms and f=20Hz.
Turn on the second pulse, and notice the frameoverlap
at long distances.
Ex 2.2: To avoid the frame overlap disc chopper are inserted in
real instruments 10-50 m from the moderator.
In this simulation merely limit the wavelength band
(set the lower limit at 0.5Å)

---
Ex 3.1: Go back to simulating just one pulse.
Place a Powder1 sample of 6mm diameter at 150 m
Set the scattering vector to q=5 Å-1
Place a TOF_cylPSD_monitor of radius 2m and height 0.2m
centered at the sample
Notice the I(t,theta) band scattered from the sample
(you might want to use a beamstop for the direct beam)
Ex 3.2: To perform a quatitative analysis
place a TOF_monitor 0.01 m wide at 40 deg scattering angle
so it is physically right after the TOF_cylPSD_monitor
Adjust the timechannels to see a detailed signal
Notice that the scattered timestructure resembles the one of
of the moderator (elastic scattering)
Calculate the peak position q and width dq form the simulated
timestructure