## Slide 1
Practical F: Build a triple-axis spectrometer!

## Slide 2: TAS essentials
Spectrometer with 3 “axes”
1. Define incoming beam ki by a monochromator crystal (Bragg’s law)

## Slide 3: TAS essentials
Spectrometer with 3 “axes”
2. A ‘sample-axis’ for zooming in on structural and dynamical aspects of the beam-sample interaction

## Slide 4: TAS essentials
Spectrometer with 3 “axes”
3. Define outgoing beam kf by an analyser crystal (Bragg’s law)

## Slide 5: TAS essentials
Spectrometer with 3 “axes”
As a start we will not add collimation or consider focusing…

## Slide 6: TAS essentials
… with these 3 axes, we can study momentum- energy-transfer in the sample-beam interaction

## Slide 7: Task 1: build a simple, non-optimised TAS (5 min)
Assume “thermal” source, e.g. parameters of ILL Thermal tube in Source_gen
  Hint: use the mcdoc utility!
“Reactor-face” TAS
  Mono:
    @ 3 m
    10x10 cm mono, PG002
    No focusing
  Sample pos:
    Start with Incoherent scatterer (cylinder 7 cm tall, 1 cm dia)
    2 m from mono
  Analyser
    @ 1m from sample
    10x10 cm mono, PG002
    No focusing
  Detector
    PSD
You can of course use other monitors along the way if you wish
Recommendation: Use Arm’s for the rotation (in- and out-going)
Recommendation: Use rotation-angles of (A1,A2) (A3,A4) (A5,A6)

## Slide 8: Once built, perform scan
Set up for 2Å neutrons at both ana and mono
Perform a “rocking curve” i.e. A1 scan
Go Go Go!!
Clock is ticking!!

## Slide 9: Let’s cheat a little: templateTAS
Lots of work done for you, including:
  Reciprocal space calculator (from original TASmad code)
  Automatic focusing options for both Mono and Ana

## Slide 10: Plus special features for this course:
New samples added, with parameters
  Single crystal related:
    SX: Flag to indicate use of Single_crystal (default 0)
    mosaic: SX mosaicity in arc minutes (default 30)
    delta_d_d: SX lattice spacing variation (default 1e-3)
    Eplus: additive energy term (SX is elastic only)
  Res_sample related:
    RES: Flat q/E resolution mode (default 0)

## Slide 11: Run a scan
Download this BCC structure to your working folder
Perform an elastic scan around (100):
And an energy-scan (no inelastic contribution from sample)
Reduce mosaic and delta_d_d to “very small” values to mimic a delta function. Use to estimate elastic resolution.
mcrun templateTAS.instr QH=1.9,2.1 QK=0 QL=0 SX=1 Sqw_coh=BCC_fake.lau -N21 -n1e4
mcrun templateTAS.instr QH=2 QK=0 QL=0 EN=-1,1 SX=1 Sqw_coh=BCC_fake.lau -N21 -n1e4

## Slide 12: Run a simulation, e.g.
mcrun templateTAS.instr QH=2 EN=0 RES=1
Use the command line util mcreplot.pl to look at the resolution ellipsoid