## Slide 1
McStas: dynamics in single crystals

## Slide 2: Sample overview reminder: Currently, SX + inelastic not so easy…
Single_crystal is elastic only….

## Slide 3: Sample overview reminder: Currently, SX + inelastic not so easy…
Phonon_simple is inelastic only….
(and BCC only…)

## Slide 4: Sample overview reminder: Currently, SX + inelastic not so easy…
Spot_sample is “not a material”, provides 𝛿-functions in Q,⍵ only

## Slide 5: Sample overview reminder: Currently, SX + inelastic not so easy…
Union components allow to combine features of Single_crystal and Phonon_simple + adds phonon polarisation

## Slide 6: Sample overview reminder: Currently, SX + inelastic not so easy…
Contribution from Duc Le, ISIS STFC is not in the code tree yet: It is unfortunately McStas 2.0
specific. Provides a “4D equivalent” of Isotropic_Sqw - and has flat sampling in that 4D-space: relatively slow, big files, requires lots of statistics

## Slide 7: But - could we do a hack maybe?
How about using Monte Carlo to choose between the different components? :-)
I.e.:
0.3 x
+
0.7 x

## Slide 8: … there is a hack, recipe:
INITIALIZE %{
declare select_sample;
%}
Arm ()
…
EXTEND %{
select_sample = rand01();
%}
COMPONENT SX= Single_crystal(…)
WHEN (select_sample < 0.3)
…
COMPONENT Phonon = Phonon_simple(…)
WHEN (select_sample >= 0.3)
…

## Slide 9: In this exercise you will have access to an instrument that uses this type of hack
The instrument is found on the DropBox:
Magnon_bcc_visualisation.instr
and needs the .lau and .comps also found there:
BCC_fake.lau
Magnon_bcc.comp
Sqq_w_monitor.com
!! PLEASE COPY FILES ACROSS - WORKING DIRECTLY IN /media/sf_Shared_folder CAN CAUSE ISSUES !!
(For the time being, skip the TAS_Magnon.instr instrument)

## Slide 10: In this exercise you will have access to an instrument that uses this type of hack
The instrument is found on the DropBox:
Magnon_bcc_visualisation.instr
and needs the .lau and .comps also found there:
BCC_fake.lau
Magnon_bcc.comp
Sqq_w_monitor.com
(For the time being, skip the TAS_Magnon.instr instrument)
New, purely inelastic component
from Kim Lefmann 2018.

## Slide 11: In this exercise you will have access to an instrument that uses this type of hack
The instrument is found on the DropBox:
Magnon_bcc_visualisation.instr
and needs the .lau and .comps also found there:
BCC_fake.lau
Magnon_bcc.comp
Sqq_w_monitor.com
(For the time being, skip the TAS_Magnon.instr instrument)
Magnons are related to spin- waves, but there are subtle
differences - Sylvain? :-)

## Slide 12
SPIN WAVES = MAGNONS
MORE GENERALY
MAGNONS : DS = 1 EXCITATIONS

## Slide 13
« Slicing a cone »

## Slide 14: Instrument contents
White-beam source
Selection between Single_crystal and Magnon_bcc.comp
A “scattering-plane” inelastic monitor that “cheats” by directly measuring ki and kf

## Slide 15: Tasks:
Locate the instrument file, compile and visualise “as usual”
In terminal run mcdoc Magnon_bcc_visualisation.instr
In terminal run mcdoc Magnon_bcc.comp and check how comp is used in the instrument file
In terminal run mcdoc Sqq_w_monitor.comp check how comp is used in the instrument file
Run a long simulation (1e7-8) and plot the results (log)

## Slide 16: Tasks - 2
5. Load and view in Matlab / iFit using:
- use the loadvol.m script from the DropBox
Vol=loadvol(’your_datadir’);

## Slide 17: Optional exercise
6. If you are longing for some more TAS :-)
  Try modifying TAS_Magnon.instr for the same Single_crystal and Magnon_bcc setup as found in the visualisation instrument
  Make it work and do some nice scans :-)

## Slide 18: Optional exercise
7. Try including a Phonon_simple instead of the Magnon_bcc component - use either of the previous instruments