## Slide 1
www.europeanspallationsource.se
15 October, 2018

## Slide 2: McStas-Mantid and the neutron pipeline
ORNL McStas workshop, October 18th-19th 2018
October 2018
Typical McStas Neuron Transport
Mantid-McStas focus:
How to analyse McStas data
Neutron Transport
Analysis
Reduction
Detector
Sample
Guide
Source

## Slide 3: Motivation: I - Highlevel
Mantid is well established software – long history
McStas is well established software – long history
Wanted to combine the reduction framework and the neutron transport framework
So users can do transport, reduction and “analysis” in one go
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 4: Motivation: II - Benefits for users
View McStas data in Mantid (simple – but nice to have)
Import McStas event data to Mantid
Use already developed and tested algorithms in Mantid to process McStas event data (no need to reinvent stuff!!!)
Advanced use: Use McStas to quantify (perhaps remove) “spurries” signal on detector (can scatt. – multi. scatt )
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 5: Illustration: simplified SANS instrument
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 6: McStas GUI: templateSANS
ORNL McStas workshop, October 18th-19th 2018
October 2018
R=150,phi=0.1, d=1,a=0

## Slide 7: Mantid GUI: templateSANS McStas data
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 8: How to use: Online documentation
Github McStas - Wiki
Nielsen, T. R.; et. al JNR 18 2015, p. 79-92.
Archive https://arxiv.org/abs/1607.02498
Built-in Mantid
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 9: TOF and pixel ID’s
Mantid was designed for data reduction at TOF spallation neutron sources
Mantid’s IDF store geometry information use in TOF analysis
This implies parsing information about:
  where the neutron source is located,
  where the sample is located,
  where each individual detector pixel is located.
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 10: The NeXus file
ORNL McStas workshop, October 18th-19th 2018
October 2018
NeXus file
Mantid
The McStas Nexus file must contain:
Event data, i.e each neutron has a pixel id and a time stamp
An IDF McStas monitor_nD gives pixle id & time for each event
mcdisplay can auto-generate an IDF

## Slide 11: McStas NeXus file
ORNL McStas workshop, October 18th-19th 2018
October 2018
Event data
IDF xml data

## Slide 12: templateSANS.inst vs templateSANS_Mantid.inst
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 13: templateSANS.inst vs templateSANS_Mantid.inst
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 14: McStas event KEYWORDS
McStas instrument file name and the McStas defined name of the instrument must be the same:
E.g. templateSANS_Mantid.instr and “DEFINE INSTRUMENT templateSANS_Mantid(…. )”
In the McStas instrument file the source must be named “sourceMantid”
E.g. "COMPONENT sourceMantid = Source_simple(…. )"
In the McStas instrument file the sample must be named “sampleMantid”
E.g. "COMPONENT sampleMantid = Sans_spheres(…. )"
In the McStas instrument file the event monitors must be named “nD_Mantid_#”
E.g. "COMPONENT nD_Mantid_1 = Monitor_nD(…. )"
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 15: How to run simulation
ORNL McStas workshop, October 18th-19th 2018
October 2018
Wiki page on GitHub

## Slide 16: McStas – Mantid: Demo Time
See how to use Mantid – McStas interface
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 17: Examples of detectors: IN5 (ILL) and LoKI (ESS)
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 18: Example: Usage of Mantid algorithms
ORNL McStas workshop, October 18th-19th 2018
October 2018
McStas – Mantid
2D scattering kernel from SasView
2D reduction in Mantid: Qxy
Can be send back to SasView fitting

## Slide 19: McStas and experimental data: SANS2D
ORNL McStas workshop, October 18th-19th 2018
October 2018
Mantid view of the McStas event data generated for the ISIS_SANS2d.instr file.
Comparison of rescaled scatting intensity I(q) derived from the experimental data and a McStas simulation. Nanospheres of radius 150 Å, polydispersion 0.2.

## Slide 20: McStas and experimental data: POWGEN
ORNL McStas workshop, October 18th-19th 2018
October 2018
By CelineD @ ESS + SNS collaboration

## Slide 21: McStas and experimental data: POWGEN
ORNL McStas workshop, October 18th-19th 2018
October 2018
By Celine D @ ESS + SNS collaboration

## Slide 22
The end …....
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 23: How to use: Generate the IDF
How-to generate McStas event data for Mantid
Step 1. Generate IDF:
mcdisplay.pl templateSANS_Mantid.instr --format=Mantid -n0
A new xml IDF file is then generated on disk
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 24: How to use: Make NeXus file for Mantid
How-to generate McStas event data for Mantid
Step 1. Compile c code:
gcc -o templateSANS_Mantid.out templateSANS_Mantid.c -DUSE_NEXUS –lNeXus –lm
Step 2. Run simulation:
templateSANS_Mantid.out --format=Nexus
Now IDF is embedded in the NeXus file to be read by Mantid
ORNL McStas workshop, October 18th-19th 2018
October 2018

## Slide 25: McStas interoperability
ORNL McStas workshop, October 18th-19th 2018
October 2018
Mantid
Neutron transport
Reduction
Data analysis