## Slide 1
5.1 STATIONARY BEAM TAILORING
(slits and collimators)
Slits and Collimators
collimator photos from :
http://www.jjxray.dk

## Slide 2
In this session:
Overview of existing Slit and Collimator components
Detailed description of the most commonly used ones
How to ‘call’ them into a *.instr file
Practical Exercise using Collimators
IMPORTANT:
All (and more) of this information can be found in the online pdf component documentation
http://www.mcstas.org/documentation/manual/mcstas-2.4.1-components.pdf
also distributed with your McStas installation
The component documentation along with the “mcdoc component_you_are_searching_for” command, are your best friends when using McStas
Slits and Collimators
5.1 STATIONARY BEAM TAILORING
(slits and collimators)

## Slide 3
Slits and Collimators
Slit (and slit-like) components:
      Slit.comp
      Beamstop.comp
      CavitiesIn.comp
      CavitiesOut.comp
Collimators:
      Collimator_linear.comp
      Collimator_radial.comp
      Collimator_ROC.comp
      Exact_radial_coll.comp
5.1 STATIONARY BEAM TAILORING
(slits and collimators)

## Slide 4
Slits and Collimators
Slit.comp
SLITS
A beam defining diaphragm
Example:
COMPONENT input_slit = Slit(xmin=-0.01, xmax=0.01, ymin=-0.01,
ymax=0.01)

## Slide 5
SLITS AND COLLIMATORS
Slits and Collimators

## Slide 6
Slits and Collimators
Beamstop.comp
A neutron absorbing area
Example:
COMPONENT stopbeam = Beamstop(xmin=-0.01, xmax=0.01, ymin=-0.01,
ymax=0.01)
COMPONENT stopbeam = Beamstop(radius=0.01)
SLITS

## Slide 7
SLITS AND COLLIMATORS
Slits and Collimators

## Slide 8
COLLIMATORS
Slits and Collimators
Collimator_linear.comp
A simple Soller blade collimator

## Slide 9
Slits and Collimators
Collimator_linear.comp
A simple Soller blade collimator
Example:
COMPONENT lin_coll = Collimator_linear(xmin=-0.1, xmax=0.1, ymin=-0.1,
ymax=0.1,length=0.25,
divergence=40,transmission=0.7)
COLLIMATORS

## Slide 10
Slits and Collimators
Collimator_radial.comp
A radial Soller blade collimator
COLLIMATORS

## Slide 11
Slits and Collimators
Collimator_radial.comp
Example:
COMPONENT rad_coll = Collimator_radial(xwidth=0.015, yheight=0.3,
        length=0.35, divergence=40.0, transmission=1,
theta_min=5, theta_max=165, nchan=128, radius=0.9)
A radial Soller blade collimator
COLLIMATORS

## Slide 13
Slits and Collimators
EXERCISE
Open the existing instrument file named ‘Test_Collimator_Radial_ex.instr’ (you will find it in today’s class folder)
This instrument file compares the performance of the ‘Collimator_Radial’ and ‘Collimator_ROC’ components. The user is requested to give an input parameter: 1 for choosing the radial collimator and 2 for using the ROC collimator.
Before running the instrument file, spend some time reading it and understanding what components it calls and what it does:
    What source is used? What type of monitors are used and what do they do?
    What is the functionality of the following lines placed after the sample component?
        EXTEND %{
        if (!SCATTERED) ABSORB;
        %}
    The file contains 2 collimator components!! Notice after each one of them the usage of a ‘WHEN ...’ statement. What does that do? (HINT: take a look at the content of the ‘INITIALIZE’ part of the file.)
COLLIMATORS

## Slide 14
Slits and Collimators
Run the ‘Test_Collimator_Radial_ex.instr’ with 1e7 neutrons
        a) with Collimator =1 (i.e. using the Collimator_radial component)
        b) with Collimator = 2 (i.e. using the Collimator_ROC component)
        Compare the results. Do the two different collimators perform similarly?
Expand the ‘Test_Collimator_Radial_ex.instr’ file, adding a third options, where the file
uses the ‘Exact_Radial_Coll.comp’ component, when the parameter Collimator=3. How does this collimator perform, compered to the previous 2?
EXERCISE
COLLIMATORS