## Slide 1: Simulation optimisation, variance reduciton, brilliance basics, FOM’s and tools
Peter Willendrup

## Slide 2: Topics
Optimising your simulation (statistics etc.)
  Variance reduction / biasing
Source brilliance and brilliance transfer
Deciding for a figure of merit
Tools: scans, iFit and guide_bot

## Slide 3: Parallelisation for better stats, brute-force… Which hammer?
Use MPI parallelisation - included in macOS install from 2.4, easy to get on Linux…
Choice of compiler and optimisation flags can at times give ~a factor of 2 in speed, cf. clang vs. Intel C
Consider if McStas 3.0 and GPU’s could help you… (see Friday talk / demo)
- BUT: Always consider if you are asking the right question if runtimes reach days/weeks… Pick the right hammer!
Sledge-hammer / brute force!
+

## Slide 4: Ensuring efficiency of the simulation is an important start…
Apply focusing techniques
  At the source (spatially, temporally, in wavelength…)
  At the sample, if possible
(carefully!) Apply SPLIT - but only if “immediately” followed by Monte Carlo choices, e.g. in sample
Alternatively use MCPL o/i which allows repetition - beware of biases! Same rule of thumb in order here.

## Slide 5: Ensuring efficiency of the simulation is an important start…
Apply focusing techniques
  At the source (spatially, temporally, in wavelength…)
  At the sample, if possible
(carefully!) Apply SPLIT - but only if “immediately” followed by Monte Carlo choices, e.g. in sample
Alternatively use MCPL o/i which allows repetition - beware of biases! Same rule of thumb in order here.
All of this can be considered “variance reduction”
or biasing
“Repeat the good neutrons that made it here…” - More on Thursday.
I/O mechanism for event files, package independent - More at the end of this section

## Slide 6: Important points to remember
Your simulation will only contain elements you provided / defined
… to the precision you defined
Answers the questions you posed
Background essentially only from “sample”, or sample-near objects
  Use concentric geometry / Union concept for sample env
  Source-term backgrounds are usually an MCNP-oriented problem (http://coimbra2016.essworkshop.org, http://istsi.essworkshop.org, https://github.com/McStasMcXtrace/SINE2020WP8)

## Slide 7: What to optimise? Figure of merit requires thought…
Also, a case-specific FOM should be chosen
    Usually not a matter of simply maximising SP flux…
    Depends strongly on the science to be done
      Typical sample size, needed q and E resolution etc.
      Relevant wavelength-band, needed dynamical range, needed resolution
      Cost (e.g. in the form of shielding requirements, guide coatings)
But brilliance-transfer is probably a good quantity to think of…

## Slide 8: FOM examples for different types of instruments
Crawford, R. K., Arai, M., Carlile, C., Chapon, L., Granroth, G., Langridge, S., ... Wiedenmann, A. (2009, Aug 26). Long-Pulse Neutron Instrumentation Workshop, August 26-28, 2009. (Oak Ridge National Laboratory ed.) Oak Ridge, USA.

## Slide 9: Neutron flux - and brilliance / brightness

## Slide 10: Neutron flux - and brilliance / brightness

## Slide 11: Neutron flux - and brilliance / brightness

## Slide 12: Neutron flux - and brilliance / brightness
10 m

## Slide 13: Neutron flux - and brilliance / brightness
10 m

## Slide 14: Neutron flux - and brilliance / brightness
10 m

## Slide 15: Liouvilles Theorem

## Slide 16: Liouvilles Theorem
12

## Slide 17: A good optic maximises transfer of brilliance
Example, elliptic guide designed by guide_bot See Thursday talk by Mads Bertelsen

## Slide 18: Simple BT-means by McStas-code? See example folder…
BTsimple, measures phase space before optic…
1.

## Slide 19: Simple BT-means by McStas-code? See example folder…
BTsimple, measures phase space before optic…
1.
Spatial ranges
Spectral range
Directional range

## Slide 20: Simple BT-means by McStas-code? See example folder…
BTsimple, measures phase space before and after optic…
1.
2.
Same phase-space element and identical binning…

## Slide 21: Simple BT-means by McStas-code? See example folder…
BTsimple, measures phase space before and after optic, calculates transferred fraction as fct. of wavelength:
Performs piece-wise division of the bins w. error propagation
1.
2.
3.

## Slide 22
BTsimple example output
1
2
3

## Slide 23: Optimisation tools…
mcrun and mcgui provide
    Simple equidistant line-scans or colinear scans par=a,b -N k. / par1=a,b par2=c,d -Nk
mcrun further provides
    -L list mode (can be non-equidistant, user chooses order, still a form of scan) par1=a,b,c,d,e,f par2=g,h,i,j,k,l
Run your simulations via iFit http://ifit.mccode.org - see http://ifit.mccode.org/McStas.html
    McStas simulation becomes an object function, monitor(s) an optimisation criterion
    Includes a host of different optimisers, e.g. particle swarms in parameter-space
    Matlab-based, perform calculations based on monitor outputs (!! use Matlab <= 2017b !!)
    Can work as a recompiled binary, but not as stable as a pure Matlab
    Use official distribution package from http://ifit.mccode.org/Downloads/iFit.zip, GitHub code is too ‘bleeding edge’ guide_bot tool is built on iFit, see Thursday talk. Mads recommends Matlab 2012 and iFit 1.3…

## Slide 24: Connectivity with other codes… Esben?

## Slide 25: By now you have been presented with most of the bricks…
Next, think of how to assemble them to solve your specific problem…