## Slide 1
McStas Introduction and general concepts

## Slide 2: Agenda
A (very) brief introduction to McStas
Components of neutron instruments
How McStas works under the hood
Components and instruments
A demo

## Slide 3: McStas: Neutrons, Monte Carlo & ray-tracing
Subatomic particle discovered by
Sir James Chadwick in 1932
,

## Slide 4: Monte Carlo techniques
Los Alamos has since then developed and perfected many different monte carlo codes leading to what is today known as the codes MCNP5 and MCNPX
State of the art is MCNP6 that features numerous (even exotic) particles
MCNP was originally Monte Carlo Neutron Photon, later N-Particle
Mainly used for high-energy particle descriptions in weapons, power reactors and routinely used for estimating dose rates and needed shielding
Not much focus on crystalline / ordered material and coherent scattering of neutrons due to the focus on high energies

## Slide 5: Examples of Monte Carlo programs
Each time physics takes place (scattering, absorption, …)
random choices are made.
Light ray-tracing: PoV-RAY and others ...
Nuclear reactor simulations etc. (general particle transport):
MCNP, Tripoli, GEANT4, FLUKA
Neutron Monte Carlo ray-tracing propagation:
McStas <www.mcstas.org>, Vitess, Restrax, NISP, IDEAS, McVine
Neutrons are described as (r, v, s, t), and are transported along
instrument models.
Propagation simply uses Newton rules, incl. gravitation.
X-ray tracing
Shadow, McXtrace, RAY, …

## Slide 6: In the big picture, McStas is this…
Classical Newtonian mechanics, i.e. and
(independent, particles though…)

## Slide 7: In the big picture, McStas is this…
Instrument
The instrument defines our “lab coordinate system”

## Slide 8: In the big picture, McStas is this…
Instrument
Component
Component
Component
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument

## Slide 9: In the big picture, McStas is this…
Instrument
Source
Sample
Monitor
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument - they have different function

## Slide 10: In the big picture, McStas is this…
Instrument
Source
Sample
Monitor
Neutrons
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument - they have different function
Neutron particles are passed on from one component to the next, changing state under way

## Slide 11: McStas is a Monte Carlo ray-tracer
Instrument
Source
Sample
Monitor
Neutrons

## Slide 12: Elements of Monte-Carlo raytracing
Instrument Monte Carlo methods implement coherent scattering effects
Uses deterministic propagation where this can be done
Uses Monte Carlo sampling of “complicated” distributions and stochastic processes and multiple outcomes with known probabilities are involved
- I.e. inside scattering matter
Uses the particle-wave duality of the neutron to switch back and forward between deterministic ray tracing and Monte Carlo approach
Result: A realistic and efficient transport of neutrons in the thermal and cold range

## Slide 13: Components of neutron instruments

## Slide 14: Components of neutron instruments
In McStas the moderator is the “source”

## Slide 15: Components of neutron instruments
In McStas the moderator is the “source”
Neutron optics include things like:
Mirrors and guides
Collimators and slits
Diskchoppers, Fermi choppers and velocity selectors
Monochromators/Analysers

## Slide 16: Components of neutron instruments
In McStas the moderator is the “source”
The sample:
Crystalline, powders, liquids, micelles, structures to image, inelastic features like phonons…
Neutron optics include things like:
Mirrors and guides
Collimators and slits
Diskchoppers, Fermi choppers and velocity selectors
Monochromators/Analysers

## Slide 17: Components of neutron instruments
In McStas the moderator is the “source”
The sample:
Crystalline, powders, liquids, micelles, structures to image, inelastic features like phonons…
Detectors are “monitors” in McStas. Mostly they act as “perfect probes” and can be positioned thought your instrument gathering 1D/2D/ event lists…
Neutron optics include things like:
Mirrors and guides
Collimators and slits
Diskchoppers, Fermi choppers and velocity selectors
Monochromators/Analysers

## Slide 18: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at DTU Physics, ILL, PSI, Uni CPH, ESS DMSC
V. 1.0 by K Nielsen & K Lefmann (1998) RISØ
Currently ~2-3 people full time plus students and user- contributions
GNU GPL license
Open Source
mcstas-users@mcstas.org mailinglist
Project website at
http://www.mcstas.org

## Slide 19: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at RISØ DTU, KU and ILL, Grenoble.
V. 1.0 by K Nielsen & K Lefmann (1998)
Currently 2.5+1 people full time plus students
4
GNU GPL license
Open Source
neutron-mc@risoe.dk mailinglist
Project website at
http://www.mcstas.org
McXtrace - since jan 2009 similar for X-rays
Synergy, knowledge transfer, shared infrastructure

## Slide 20: Used in many places

## Slide 21: What is McStas used for?
Instrumentation
Planning
Construction
Virtual experiments
Data analysis
Teaching
(KU, DTU)

## Slide 22: Reliability - cross comparisons
Much effort has gone into this
Here: simulations vs. exp. at powder diffract. DMC, PSI
The bottom line is
McStas agree very well with other packages (NISP, Vitess, IDEAS, RESTRAX, ...)
Experimental line shapes are within 5%
Absolute intensities are within 10%
Common understanding: McStas and similar codes are reliable
P. Willendrup et al., Physica B, 386, (2006), 1032.
E. Farhi, P. Willendrup, from IN22 benchmark exp.

## Slide 23: McStas overview
Portable code (Unix/Linux/Mac/Windoze)
Ran on everything from iPhone to 1000+ node cluster!
'Component' files (~100) inserted from library
    Sources
    Optics
    Samples
    Monitors
    If needed, write your own comps
DSL + ISO-C code gen.
CPU’s
+ NVIDIA GPU’s

## Slide 24: Under-the-hood / inner workings
Domain-specific-language (DSL) based on compiler technology (LeX+Yacc)
    Simple Instrument language ISO C
Component codes realizing beamline parts (including user contribs)
Library of common functions for e.g.
    I/O
    Random numbers
    Physical constants
    Propagation
    Precession in fields
    ...
Code generation

## Slide 25: Implementation

## Slide 26: Placing components - source
One of the first components in your instrument is typically a source, which has a coordinate system like this….
z is along neutron beam direction
y is vertical
x at an angle of 90° wrt. z,y
x
y
z
Right-handed
coordinate system

## Slide 27: Placing components - source
Often the source coordinate system coincides with the “lab” coordinate system, denoted ABSOLUTE in McStas language, i.e.
COMPONENT Source = Source_simple(…) AT (0,0,0) ABSOLUTE
x
y
z

## Slide 28: Placing further components - RELATIVE
Placing further components is done by order of 1. Location, i.e
COMPONENT Source = Source_simple(…) AT (0,0,0) ABSOLUTE
x
y
z
x´
y´
z’
COMPONENT Guide = Guide(…) AT (0,0,1) RELATIVE Source

## Slide 29: Placing further components - RELATIVE
Placing further components is done by order of 2. Rotation, i.e
COMPONENT Source = Source_simple(…) AT (0,0,0) ABSOLUTE
x
y
z
x´
y´
z’
x”
z”
COMPONENT Guide = Guide(…) AT (0,0,1) RELATIVE Source
ROTATED (0,30,0) RELATIVE Source
(Reference labels can also be PREVIOUS or PREVIOUS+1 etc.)

## Slide 30: Components often have their origin at the centre of mass, i.e. for samples … but not for neutron guides
x´
y´
z’
x
y
z
Generally speaking, the component author can choose
the meaningful coordinate system for the given problem!
- The McStas system takes care of the transformation between them….

## Slide 31: Component geometries are typically simple objects… But some have polygon-description of the surface
2D
3D

## Slide 32: Component classes
Sources - these define MC starting conditions / “inject” neutrons to our simulation
Optics - used to tailor properties of the neutron beam
  Examples are mirrors, guides, choppers, collimators, slits, …
Samples - “matter” of some form
  Powders, single crystals, liquids, micelles in solution, reflecting surfaces…
Monitors - may probe the state of the neutron beam and store histograms / event lists
Misc, obsolete
  “Other stuff” and “Old stuff”

## Slide 33: Component classes
Sources - these define MC starting conditions / “inject” neutrons to our simulation
Optics - used to tailor properties of the neutron beam
  Examples are mirrors, guides, choppers, collimators, slits, …
Samples - “matter” of some form
  Powders, single crystals, liquids, micelles in solution, reflecting surfaces…
Monitors - may probe the state of the neutron beam and store histograms / event lists
Misc, obsolete
  “Other stuff” and “Old stuff”
Common to all components:
They set, manipulate/interact with
or measure the state of the neutron (ray)

## Slide 34: Neutron sources, i.e. moderators
To first order emit uniformly into steradian

## Slide 35: Neutron sources, i.e. moderators
Generally we are intersted in the input to a single instrument, characterised by a certain solid angle , often corresponding to a rectangle x at a distance from the source
E.g. the beamport?

## Slide 36: Neutron sources, i.e. moderators
The emmission intensity into our chosen solid angle can be a function of wavelength, time (pulsed sources) and possibly point of origin on the source surface
The emission of particles into the solid angle is in fact an integration and leads to a simulated “intensity” of .
In McStas, that integrated intensity is partitioned over a given set of particle rays referred to as ncount, -n or --ncount
The default ncount is 1e6 rays

## Slide 37: Neutron sources, i.e. moderators
Our neutron rays are emitted randomly, sampling and all variables of the source “spectrum”, i.e. wavelength, time and area
assigning neutron weights such that

## Slide 38: Neutron rays in McStas - what are they?
The starting point on the surface, i.e. (in the code variables x,y,z)
The direction into and our / (in the code variables vx,vy,vz)
The starting time (in the code the variable t)
The initial intensity / weight of the neutron ray (in the code the variable p)
If needed the initial polarisation (in the code the variables sx,sy,sz)
Neutron ray in McStas:
Location x,y,z
Velocity vx,vy,vz
Time t
Polarisation. sx,sy,sz
Intensity p
Defining the neutron starting conditions imply setting:

## Slide 39: Neutron (ray)-matter interaction 1: reflecting surface
1 starting situation
Neutron ray
Mirror surface
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0

## Slide 40: Neutron (ray)-matter interaction 1: reflecting surface
2. Propagate to the mirror surface
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
1
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0

## Slide 41: Neutron (ray)-matter interaction 1: reflecting surface
3. Checks (are we on surface, what is probability of reflection etc.)
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
1
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0

## Slide 42: Neutron (ray)-matter interaction 1: reflecting surface
4. Reflect
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
1
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
2
Weight of final ray is adjusted according to reflectivity, see next slide

## Slide 43: Parametrisation of reflectivity on mirrors etc.
d
R
(i.e. Q is calculated for given neutron, reflectivity encoded in changed p value)

## Slide 44: Neutron (ray)-matter interaction in General
A neutron hitting a sample can be:
absorbed, transmitted, or scattered

## Slide 45
For a non-thin sample the probabilities for absorption, transmission or scattering are given by
t = sample thickness
microscopic cross section [barn/atom]
1 barn = 10-24cm2
number density [atoms/cm3]
macroscopic cross section [cm-1]
Samples

## Slide 46
Samples/Matter interaction in General in McStas
A neutron ray hitting a sample can be:
transmitted+absorption, or scattered+absorption

## Slide 47: Transport of weight through the instrument…
The weight multiplier of the j’th component, , is calculated by the probability rule where Pb is the physical probability for the event ”b“, and is the probability that the Monte Carlo simulation selects this event.
In case of “branching”, i.e. multiple outcomes, it is clear that
Instrument
Source
Sample
Monitor
In a given component, the neutron intensity is adjusted by a multiplicative factor (probability)

## Slide 48: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Starting at the source

## Slide 49: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to first comp in the list

## Slide 50: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_neutron=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.

## Slide 51: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_neutron=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.
The order of components is important,
and in general overlaps should be avoided!

## Slide 52: Units used - and differences to Vitess
Generally SI-Units, e.g. meters and seconds etc.
Added neutron-scattering meaningful quantities of E[meV], 𝝺[Å] and cross sections in 𝞂 [barns]
Main differences / difficulties translating between McStas Vitess
Different length-units for placement / sizes [m] [cm]
Different propagation-coordinate system
McStas explicitly and automatically contains “free space”, Vitess has this “inside” the modules or by adding “spacewindow”
Sources in McStas always propagates “by virtual window”, i.e. does not itself propagate
z || beam
y vertical
x ⊥ beam
x || beam
z vertical
y ⊥ beam

## Slide 53: McStas Vitess compatibility features
MCPL particle list is supported from McStas 2.3- (2016) and Vitess 3.4 (2018)
McStas includes Vitess_output and Vitess_input, but better use MCPL
mcstas2vitess can be used to port McStas components to Vitess
Vitess_ChopperFermi is the Vitess Fermi chopper ported to McStas
Friendly competition and collaboration for 1.5 decades! - e.g. Klaus Lieutenant was part of McStas team for 2 years

## Slide 54: Instrument file

## Slide 55: Component file

## Slide 56: Generated c-code

## Slide 57: Writing new comps or understanding existing is not that complex...
Check our long list of components and look inside... Most of them are quite simple and short... Statistics:
(update: 175)
Number of lines of code per component - 240 comps in total
# Lines of code (log axis)

## Slide 58: Writing new comps or understanding existing is not that complex...
Check our long list of components and look inside... Most of them are quite simple and short... Statistics:
(update: 175)
Number of lines of code per component - 240 comps in total
Well-developed community support
  30-40% of existing and new additions are from users
  No direct refereeing of the code, but these requirements:
      At least one test-instrument
      Meaningful documentation headers (in-code docs)
  Contributions go in dedicated contrib/ section of library

## Slide 59: Example suite: ~252 instruments