## Slide 2: McStas and how-to generate event data for Mantid and scipp
Torben

## Slide 3: McStas and McStasScript
Histogram data / binned data / ascii data
mcgui

## Slide 4: McStas event data and The NeXus file
Process McStas event data as you would do with recorded data from a beamline
NeXus file
Mantid
https://www.nexusformat.org
The McStas Nexus file must contain:
Event data, i.e. each neutron has a pixel id and a time stamp
An IDF McStas monitor_nD gives pixle id & time for each event
mcdisplay can auto-generate an IDF

## Slide 5: McStas NeXus file
Mantid/scipp compatible

## Slide 6: How to use: Online documentation
Github McStas wiki pages
Archive - lanl.arXiv.org
Docs in Mantid/scipp
6

## Slide 7: IDF xml data, TOF and pixel ID’s
Mantid’s IDF stores geometry information used in TOF analysis
This implies parsing information about:
  where the neutron source is located,
  where the sample is located,
  where each individual detector pixel is located.

## Slide 8: McStas event KEYWORDS
McStas instrument file name and the McStas defined name of the instrument must be the same:
E.g. templateSANS_Mantid.instr and “DEFINE INSTRUMENT templateSANS_Mantid(…. )”
In the McStas instrument file the source must be named “sourceMantid”
E.g. "COMPONENT sourceMantid = Source_simple(…. )"
In the McStas instrument file the sample must be named “sampleMantid”
E.g. "COMPONENT sampleMantid = Sans_spheres(…. )"
In the McStas instrument file the event monitors must be named “nD_Mantid_#”
E.g. "COMPONENT nD_Mantid_1 = Monitor_nD(…. )"

## Slide 9: templateSANS.inst vs templateSANS_Mantid.inst

## Slide 10: templateSANS.inst vs templateSANS_Mantid.inst

## Slide 11: Examples of detectors: IN5 (ILL) and LoKI (ESS)
A banana shaped monitor
Off file geometry

## Slide 12: McStas and experimental data: POWGEN
By CelineD @ ESS + SNS collaboration

## Slide 13: How to use: How to run simulation
Github wiki pages

## Slide 14: How to use CLI: Generate the IDF
How-to generate McStas event data for Mantid/scipp
Step 1. Generate c file:
mcstas templateSANS_Mantid.instr --trace
Step 2. Generate IDF:
mcdisplay-mantid.pl templateSANS_Mantid.instr -n0
A new xml IDF file is then generated on disk

## Slide 15: How to use CLI: Make NeXus file for Mantid/scipp
How-to generate McStas event data for Mantid/scipp
Step 1. Compile c code:
gcc -o templateSANS_Mantid.out templateSANS_Mantid.c -DUSE_NEXUS –lNeXus –lm -I/usr/include/nexus
Step 2. Run simulation:
templateSANS_Mantid.out --format=Nexus
Now IDF is embedded in the NeXus file to be read by Mantid/scipp

## Slide 17: Demo
Let’s try to do a test . . . . . . .

## Slide 19: Exercise
* choose your instrument
* compile and run (use 2.7.1)
* load into scipp
* view instrument
* plot monitors (in scipp)
Compile a Mantid/scipp instrument and generate event data

## Slide 20: Finish presentation