## Slide 1: McStas and McXtrace: simulation tools for neutron- and X-ray instruments
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
Peter Willendrup1,2, Erik Knudsen1
1NEXMAP, Physics Department, Technical University of Denmark, Denmark
2ESS Data Management & Sofware Center, Denmark

## Slide 2: Agenda
Introduction to McStas & McXtrace
Neutrons and X-rays
Monte Carlo method
Ray-tracing
Components of scattering instruments
A short description of this afternoons exercise
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 3: McStas & McXtrace
In some sense you already “know” these codes… They are what you have been running in the elearn1 “simulator”
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 4: Purpose of today’s activities
See what is “under the hood” in the simulator - and work with it!
Produce an instrument model
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 5: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at DTU Physics, ILL, PSI, Uni CPH, ESS
V. 1.0 by K Nielsen & K Lefmann (1998) RISØ
Currently ~ 4 people full time plus students
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
GNU GPL license
Open Source
mcstas-users@mcstas.org mailinglist
Project website at
http://www.mcstas.org

## Slide 6
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
McXtrace - same idea, but for X-rays (2009-)

## Slide 7: Both neutrons and X-rays interact with atoms
X-rays “see” the electron cloud surrounding the atomic nucleus – the higher atomic no. ‘Z’, the more scattering
In contrast neutrons “see” the nucleus – no simple connection between level of scattering and atomic no.
Result: Two very different response/contrasts
Large contrast H vs D,
ideal for biological systems,
via deuteration
Neutron magnetic moment,
sensitivity to magnetical structures,
polarization techniques (Larmor)

## Slide 8: Both neutrons and X-rays interact with atoms
X-rays “see” the electron cloud surrounding the atomic nucleus – the higher atomic no. ‘Z’, the more scattering
In contrast neutrons “see” the nucleus – no simple connection between level of scattering and atomic no.
Result: Two very different response/contrasts
Low velocities makes beam-tailoring
using mechanical devices feasible

## Slide 9: Monte Carlo techniques
During WW2, “numerical experiments” were applied at Los Alamos for solving mathematical complications of computing fission, criticality, neutronics, hydrodynamics, thermonuclear detonation etc.
Notable fathers: John v. Neumann Stanislav Ulam Nicholas Metropolis
Named “Monte Carlo” after Ulam’s fathers frequent visits to the Monte Carlo casino in Las Vegas
Initially “implemented” by letting large numbers of women use tabularized random numbers and hand calculators for individual particle calculations
Later, analogue and digital computing devices were used
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 10: Ray-tracing methods
When neutrons move in “free space”, we use ray-tracing - but in most cases in direction source -> detector
Of course parabolas rather than straight lines are uses to implement gravity
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 11: Overall picture: Monte Carlo Ray-Tracing
Important efficiency mechanisms:
    “Focusing” - e.g. source to beamport only (4π vs. limited solid angle only)
    Rather vs. single particle description, absorption handled though statistics and downscaling the ray weight
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 12: What are the codes used for?
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
Instrumentation
Virtual experiments
Data analysis
Teaching
(KU, DTU)

## Slide 13: McStas: key concepts
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
n
n
Time (t)
Local, internal coordinate system!

## Slide 14: McStas: key concepts
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
X
X
Time (t)
Local, internal coordinate system!
X-ray package:
Weight (p), # photons (left) in the package
Coordinates (x,y,z)
Wavevector (kx,ky,kz)
Polarization (Ex,Ey,Ez)
Phase ( )
Time(t)
X-ray

## Slide 15: McStas/McXtrace tech overview
Portable code (Unix/Linux/Mac/Windoze)
Ran on everything from iPhone to 1000+ node cluster!
'Component' files (~150/~40) inserted from library
    Sources
    Optics
    Samples
    Monitors
    If needed, write your own comps
DSL + ISO-C code gen.
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
Instrument file (average
user, point/click, DSL)
Component (advanced user, modify from
existing, c-code)
Kernel
(McCode team)

## Slide 16: Sources - 1
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
X-ray sources
  Lab equipment
    X-ray tube
    Rotating anode
    Liquid jet anode
  Synchrotron
    Bending magnet
    Wiggler
    Undulator
  XFEL
    SASE (very long undulator)
Neutron sources
  Lab equipment
    Radioisotope-based
    CANS (Compact accellerator based)
  Steady state sources
    Research reactors
    Spallation source at PSI
  Pulsed sources
    Spallation sources, SP LP
    Pulsed reactor (Dubna)
  Most neutron sources require moderation of the neutron energy

## Slide 17: Sources - 2
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
X-ray sources
  Lab equipment
    X-ray tube
    Rotating anode
    Liquid jet anode
  Synchrotron
    Bending magnet
    Wiggler
    Undulator
  XFEL
    SASE (very long undulator)
Neutron sources

## Slide 18: Spatial / directional beam adjustment
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
Spatial: pinholes / slits / apertures
  Static or adjustable “hole” in absorbing material
Directional: slit-assemblies or collimators
  Two or more slits defines an accepted divergence
  Collimators makes “channels”, typically with absorbing walls
  Usually static devices, but rotating radial collimators exist

## Slide 19: Temporal beam adjustment, rotating optics
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
X-ray and neutrons
  Choppers
Neutrons only - monochromating rotating optics
  Fermi-chopper “rotating collimator” Velocity-selector

## Slide 20: Crystal-based monochromators - Braggs law
McStas and McXtrace: simulation tools for neutron- and X-ray instruments
X-ray
  Typically very little mosaicity (perfect single crystal Si, Ge, C,…)
  Laue and Bragg geometries (transmission vs. reflection)
  Creates narrow, low-divergence monochromatic beams
Neutron
  Typically high-mosaicity (pyrolytic graphite, deformated Cu, Ge, …)
  Often focusing, multi-crystal
  Typically Bragg geometry (reflection)
  Creates medium divergence monochromatic beams

## Slide 21
X-ray
  Refractive lenses (CRLs)
  Kinoform Lens
  Fresnel Zone Plates
Refractive optics
Neutron
  Refractive Lenses (CRLs)
    Magnetic Materials (focusing e.g. “spin-up”)

## Slide 22
Refractive optics, total reflection - a reminder
n2=1
n1>1
Visible light
Absorption term
Refraction term

## Slide 23
Refractive optics
X-ray
  Refractive index < 1
Neutron
  Refractive Index < 1 for b>1
  With neutrons, Lens effect from magnetism is small, hence “CRL”
Low Z materials with low absorption. Be, Al.
High b materials with low absorption. Mg2F
CRL’s are a reasonable way to have low absorption with
sufficient refraction

## Slide 24
Multilayers
X-ray and neutrons
Playing with phase of partial ray reflected from a given layer in the structure

## Slide 25
Multilayers
X-rays:
Superstructure often used as “monochromator” - also in focusing geometry
When used as monochromator, use one of the first “side peaks” on the reflectivity curve

## Slide 26
Neutrons:
Superstructure “extends” the total-reflection range in Q by “Bragg peaks”
ideally a wide, flat distribution
used in all kinds of neutron optics, but specifically in guides - “optical fibre”
Multilayers

## Slide 27: Example suite - instruments: 247 McStas 63 McXtrace
McStas and McXtrace: simulation tools for neutron- and X-ray instruments

## Slide 28: Questions?