## Slide 1
McStas Introduction and general concepts
2021 Virtual ISIS McStas School, April 13th-15th 2021

## Slide 2: Agenda
A (very) brief introduction to McStas
Components of neutron instruments
How McStas works under the hood
Components and instruments
A demo

## Slide 3: In the big picture, McStas is this…
Classical Newtonian mechanics, i.e. and
(independent, particles though…)

## Slide 4: In the big picture, McStas is this…
Instrument
The instrument defines our “lab coordinate system”

## Slide 5: In the big picture, McStas is this…
Instrument
Component
Component
Component
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument

## Slide 6: In the big picture, McStas is this…
Instrument
Source
Sample
Monitor
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument - they have different function

## Slide 7: In the big picture, McStas is this…
Instrument
Source
Sample
Monitor
Neutrons
The instrument defines our “lab coordinate system”
The components define devices or features available in our instrument - they have different function
Neutron particles are passed on from one component to the next, changing state under way

## Slide 8: McStas is a Monte Carlo ray-tracer
Instrument
Source
Sample
Monitor
Neutrons

## Slide 9: Elements of Monte-Carlo raytracing
Instrument Monte Carlo methods implement coherent scattering effects
Uses deterministic propagation where this can be done
Uses Monte Carlo sampling of “complicated” distributions and stochastic processes and multiple outcomes with known probabilities are involved
- I.e. inside scattering matter
Uses the particle-wave duality of the neutron to switch back and forward between deterministic ray tracing and Monte Carlo approach
Result: A realistic and efficient transport of neutrons in the thermal and cold range

## Slide 10: Components of neutron instruments

## Slide 11: Components of neutron instruments
In McStas the moderator is the “source”

## Slide 12: Components of neutron instruments
Neutron optics include things like:
Mirrors and guides
Collimators and slits
Diskchoppers, Fermi choppers and velocity selectors
Monochromators/Analysers
In McStas the moderator is the “source”

## Slide 13: Components of neutron instruments
Neutron optics include things like:
Mirrors and guides
Collimators and slits
Diskchoppers, Fermi choppers and velocity selectors
Monochromators/Analysers
In McStas the moderator is the “source”
The sample:
Crystalline, powders, liquids, micelles, structures to image, inelastic features like phonons…

## Slide 14: Components of neutron instruments
Neutron optics include things like:
Mirrors and guides
Collimators and slits
Diskchoppers, Fermi choppers and velocity selectors
Monochromators/Analysers
In McStas the moderator is the “source”
The sample:
Crystalline, powders, liquids, micelles, structures to image, inelastic features like phonons…
Detectors are “monitors” in McStas. Mostly they act as “perfect probes” and can be positioned thought your instrument gathering 1D/2D/ event lists…

## Slide 15: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at DTU Physics, ILL, PSI, Uni CPH, ESS DMSC
V. 1.0 by K Nielsen & K Lefmann (1998) RISØ
Currently 2.5+1 people full time plus students
GNU GPL license
Open Source
mcstas-users@mcstas.org mailinglist
Project website at
http://www.mcstas.org

## Slide 16: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at RISØ DTU, KU and ILL, Grenoble.
V. 1.0 by K Nielsen & K Lefmann (1998)
Currently 2.5+1 people full time plus students
4
GNU GPL license
Open Source
neutron-mc@risoe.dk mailinglist
Project website at
http://www.mcstas.org
McXtrace - since jan 2009 similar for X-rays
Synergy, knowledge transfer, shared infrastructure

## Slide 17: Used in many places

## Slide 18: What is McStas used for?
Instrumentation
Planning
Construction
Virtual experiments
Data analysis
Teaching
(KU, DTU)

## Slide 19: Reliability - cross comparisons
Much effort has gone into this
Here: simulations vs. exp. at powder diffract. DMC, PSI
The bottom line is
McStas agree very well with other packages (NISP, Vitess, IDEAS, RESTRAX, ...)
Experimental line shapes are within 5%
Absolute intensities are within 10%
Common understanding: McStas and similar codes are reliable
P. Willendrup et al., Physica B, 386, (2006), 1032.
E. Farhi, P. Willendrup

## Slide 20: McStas overview
Portable code (Unix/Linux/Mac/Windoze)
Ran on everything from iPhone to 1000+ node cluster!
'Component' files (~100) inserted from library
    Sources
    Optics
    Samples
    Monitors
    If needed, write your own comps
DSL + ISO-C code gen.

## Slide 21: Under-the-hood / inner workings
Domain-specific-language (DSL) based on compiler technology (LeX+Yacc)
    Simple Instrument language ISO C
Component codes realizing beamline parts (including user contribs)
Library of common functions for e.g.
    I/O
    Random numbers
    Physical constants
    Propagation
    Precession in fields
    ...
Code generation

## Slide 22: Implementation

## Slide 23: Placing components - source
One of the first components in your instrument is typically a source, which has a coordinate system like this….
z is along neutron beam direction
y is vertical
x at an angle of 90° wrt. z,y
x
y
z
Right-handed
coordinate system

## Slide 24: Placing components - source
Often the source coordinate system coincides with the “lab” coordinate system, denoted ABSOLUTE in McStas language, i.e.
COMPONENT Source = Source_simple(…) AT (0,0,0) ABSOLUTE
x
y
z

## Slide 25: Placing further components - RELATIVE
Placing further components is done by order of 1. Location, i.e
COMPONENT Source = Source_simple(…) AT (0,0,0) ABSOLUTE
x
y
z
x´
y´
z’
COMPONENT Guide = Guide(…) AT (0,0,1) RELATIVE Source

## Slide 26: Placing further components - RELATIVE
Placing further components is done by order of 2. Rotation, i.e
COMPONENT Source = Source_simple(…) AT (0,0,0) ABSOLUTE
x
y
z
x´
y´
z’
x”
z”
COMPONENT Guide = Guide(…) AT (0,0,1) RELATIVE Source
ROTATED (0,30,0) RELATIVE Source
(Reference labels can also be PREVIOUS or PREVIOUS+1 etc.)

## Slide 27: Components often have their origin at the centre of mass, i.e. for samples … but not for neutron guides
x´
y´
z’
x
y
z
Generally speaking, the component author can choose
the meaningful coordinate system for the given problem!
- The McStas system takes care of the transformation between them….

## Slide 28: Component geometries are typically simple objects… But some have polygon-description of the surface
2D
3D

## Slide 29: Component classes
Sources - these define MC starting conditions / “inject” neutrons to our simulation
Optics - used to tailor properties of the neutron beam
  Examples are mirrors, guides, choppers, collimators, slits, …
Samples - “matter” of some form
  Powders, single crystals, liquids, micelles in solution, reflecting surfaces…
Monitors - may probe the state of the neutron beam and store histograms / event lists
Misc, obsolete
  “Other stuff” and “Old stuff”

## Slide 30: Component classes
Sources - these define MC starting conditions / “inject” neutrons to our simulation
Optics - used to tailor properties of the neutron beam
  Examples are mirrors, guides, choppers, collimators, slits, …
Samples - “matter” of some form
  Powders, single crystals, liquids, micelles in solution, reflecting surfaces…
Monitors - may probe the state of the neutron beam and store histograms / event lists
Misc, obsolete
  “Other stuff” and “Old stuff”
Common to all components:
They set, manipulate/interact with
or measure the state of the neutron (ray)

## Slide 31: Neutron sources, i.e. moderators
To first order emit uniformly into steradian

## Slide 32: Neutron sources, i.e. moderators
Generally we are intersted in the input to a single instrument, characterised by a certain solid angle , often corresponding to a rectangle x at a distance from the source
E.g. the beamport?

## Slide 33: Neutron sources, i.e. moderators
The emmission intensity into our chosen solid angle can be a function of wavelength, time (pulsed sources) and possibly point of origin on the source surface
The emission of particles into the solid angle is in fact an integration and leads to a simulated “intensity” of .
In McStas, that integrated intensity is partitioned over a given set of particle rays referred to as ncount, -n or --ncount
The default ncount is 1e6 rays

## Slide 34: Neutron sources, i.e. moderators
Our neutron rays are emitted randomly, sampling and all variables of the source “spectrum”, i.e. wavelength, time and area
assigning neutron weights such that

## Slide 35: Neutron rays in McStas - what are they?
The starting point on the surface, i.e. (in the code variables x,y,z)
The direction into and our / (in the code variables vx,vy,vz)
The starting time (in the code the variable t)
The initial intensity / weight of the neutron ray (in the code the variable p)
If needed the initial polarisation (in the code the variables sx,sy,sz)
Neutron ray in McStas:
Location x,y,z
Velocity vx,vy,vz
Time t
Polarisation. sx,sy,sz
Intensity p
Defining the neutron starting conditions imply setting:

## Slide 36: Neutron (ray)-matter interaction 1: reflecting surface
1 starting situation
Neutron ray
Mirror surface
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0

## Slide 37: Neutron (ray)-matter interaction 1: reflecting surface
2. Propagate to the mirror surface
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
1
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0

## Slide 38: Neutron (ray)-matter interaction 1: reflecting surface
3. Checks (are we on surface, what is probability of reflection etc.)
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
1
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0

## Slide 39: Neutron (ray)-matter interaction 1: reflecting surface
4. Reflect
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
1
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
0
(x,y,z,vx,vy,vz,t,sx,sy,sz,p)
2
Weight of final ray is adjusted according to reflectivity, see next slide

## Slide 40: Parametrisation of reflectivity on mirrors etc.
d
R
(i.e. Q is calculated for given neutron, reflectivity encoded in changed p value)

## Slide 41: Neutron (ray)-matter interaction in General
A neutron hitting a sample can be:
absorbed, transmitted, or scattered

## Slide 42
For a non-thin sample the probabilities for absorption, transmission or scattering are given by
t = sample thickness
microscopic cross section [barn/atom]
1 barn = 10-24cm2
number density [atoms/cm3]
macroscopic cross section [cm-1]
Samples

## Slide 43
Samples/Matter interaction in General in McStas
A neutron ray hitting a sample can be:
transmitted+absorption, or scattered+absorption

## Slide 44: Transport of weight through the instrument…
The weight multiplier of the j’th component, , is calculated by the probability rule where Pb is the physical probability for the event ”b“, and is the probability that the Monte Carlo simulation selects this event.
In case of “branching”, i.e. multiple outcomes, it is clear that
Instrument
Source
Sample
Monitor
In a given component, the neutron intensity is adjusted by a multiplicative factor (probability)

## Slide 45: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Starting at the source

## Slide 46: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to first comp in the list

## Slide 47: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_neutron=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.

## Slide 48: To first order, McStas is linear and follows sequence of components in your file…
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_neutron=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.
The order of components is important,
and in general overlaps should be avoided!

## Slide 49: Instrument file

## Slide 50: Component file

## Slide 51: Generated c-code

## Slide 52: Writing new comps or understanding existing is not that complex...
Check our long list of components and look inside... Most of them are quite simple and short... Statistics:
(update: 175)
Number of lines of code per component - 199 comps in total
# Lines of code (log axis)

## Slide 53: Writing new comps or understanding existing is not that complex...
Check our long list of components and look inside... Most of them are quite simple and short... Statistics:
(update: 175)
Number of lines of code per component - 199 comps in total
Well-developed community support
  30-40% of existing and new additions are from users
  No direct refereeing of the code, but these requirements:
      At least one test-instrument
      Meaningful documentation headers (in-code docs)
  Contributions go in dedicated contrib/ section of library

## Slide 54: Example suite: ~140 instruments

## Slide 55
Your HighNESS…

## Slide 56: Units used - and differences to Vitess
Generally SI-Units, e.g. meters and seconds etc.
Added neutron-scattering meaningful quantities of E[meV], 𝝺[Å] and cross sections in 𝞂 [barns]
Main differences / difficulties translating between McStas Vitess
Different length-units for placement / sizes [m] [cm]
Different propagation-coordinate system
McStas explicitly and automatically contains “free space”, Vitess has this “inside” the modules or by adding “spacewindow”
Sources in McStas always propagates “by virtual window”, i.e. does not itself propagate
z || beam
y vertical
x ⊥ beam
x || beam
z vertical
y ⊥ beam

## Slide 57: McStas Vitess compatibility features
MCPL particle list is supported from McStas 2.3- (2016) and Vitess 3.4 (2018)
McStas includes Vitess_output and Vitess_input, but better use MCPL
mcstas2vitess can be used to port McStas components to Vitess
Vitess_ChopperFermi is the Vitess Fermi chopper ported to McStas
Friendly competition and collaboration for 1.5 decades! - e.g. Klaus Lieutenant was part of McStas team for 2 years

## Slide 58: McStas: Neutrons, Monte Carlo & ray-tracing
Subatomic particle discovered by
Sir James Chadwick in 1932
,

## Slide 59: Neutron facilities

## Slide 60: Monte Carlo techniques
Los Alamos has since then developed and perfected many different monte carlo codes leading to what is today known as the codes MCNP5 and MCNPX
State of the art is MCNP6 that features numerous (even exotic) particles
MCNP was originally Monte Carlo Neutron Photon, later N-Particle
Mainly used for high-energy particle descriptions in weapons, power reactors and routinely used for estimating dose rates and needed shielding
Does not to date handle crystalline / ordered material and coherent scattering of neutrons due to the focus on high energies

## Slide 61: Examples of Monte Carlo programs
Each time physics takes place (scattering, absorption, …)
random choices are made.
Light ray-tracing: PoV-RAY and others ...
Nuclear reactor simulations (neutron transport):
MCNP, Tripoli, GEANT4, FLUKA
Neutron Ray-Tracing propagation:
McStas <www.mcstas.org>, Vitess, Restrax, NISP, IDEAS, McVine
Neutrons are described as (r, v, s, t), and are transported along
instrument models.
Propagation simply uses Newton rules, incl. gravitation.
X-ray tracing
Shadow, McXtrace, RAY, …