From modelling to McStas and more
A short guide
E. Farhi, ILL

---
Data formats

---
McStas Data formats
McStas uses a number of input data formats, all text based.
Lau (Single_crystal, PowderN, Isotropic_Sqw)
Laz (PowderN, Isotropic_Sqw)
Sqw (Isotropic_Sqw)
qSq (Isotropic_Sqw) – mostly for liquids
nxs (Sample_nxs) – this is not a NeXus/HDF
PDB (SANSPDB)
The question is how to generate these files…
By hand ?

---
Material modelling formats
- MD (classical or DFT)
  - trajectories, many data formats
- Lattice dynamics:
  - PhonoPy FORCE_SETS
  - ...

---
Nuclear data base formats
- ENDF, JEFF, JENDL, …
  - all use a standard format for a set of materials. Most are monoatomic / incoherent
- ACE
  - Same as ENDF, but in binary for MCNP

---
Experiments
- Intensity(d) → F(Q) → S(Q) and Laz
- Intensity(HKL) → F2(HKL) → Lau
- Intensity(theta,ToF) → S(q,w)
- Often saved as text and/or NeXus

---
Tools
- iFit
- Mantid
- Python/ASE (IO)
- MDANSE/nMoldyn (converters)
- Scripts of all kinds
  - OpenBABEL, ...
- cif2hkl
- bash

---
Material DataBases
- ICSD <http://icsd.ill.fr/icsd/index.html>
- COD <http://crystallography.net>
- <https://www.materialsproject.org/>
- PhononDB <http://phonondb.mtl.kyoto-u.ac.jp/>
- Nomad <https://repository.nomad-coe.eu/>
Mostly provide structures...

---
McStas: structure: powder
- For powders, the pure elastic diffraction is easy to prepare: LAZ
  - PowderN
  - Single_crystal(powder=1, ...)
  - Isotropic_Sqw
Terminal:
cif2hkl --powder file.cif
CIF file
FullProf/ShelX
McStas Laz file
iFit:
cif2hkl(‘file.cif’,’’,’p’)
CIF file
FullProf/ShelX
McStas Laz file

---
McStas: structure: SX
- For single crystals, the pure elastic diffraction is easy to prepare: LAU
  - PowderN
  - Single_crystal
  - Isotropic_Sqw
Terminal:
cif2hkl --xtal file.cif
CIF file
FullProf/ShelX
McStas Lau file
iFit:
cif2hkl(‘file.cif’,’’,’x’)
CIF file
FullProf/ShelX
McStas Lau file

---
McStas: structure: COD
- Cif2hkl from iFit can input chemical formula
- Requires internet connection to COD
iFit:
cif2hkl(‘cod: La Mn O3’,’’,’p’)
Chemical formula
McStas Laz file
iFit:
cif2hkl(‘cod: O3 Sr Ti’,’’,’p’)
Chemical formula
McStas Lau file

---
McStas: structure: others
- Other McStas structure file formats
  - SANSPDB and similars: get from Data Bases
  - Sample_nxs: manual edit only (nxs, text)
  - Isotropic_Sqw: manual edit only (qSq, text)
  - NCrystal_sample*: (ncmat,nxs,lau)
Terminal:
babel -iFMT -oOUT file.cif
FMT file
OUT file
Terminal:
babel -icif -opdb file.cif
CIF file
PDB
OpenBabel supports many data files
*in McStas from v. 2.5

---
McStas: dyn from ToF spec
- Import and correct data with e.g. LAMP, Mantid
- Integrate radially (|q|) and compute S(q,w)
- Export to e.g. HDF/NeXus or other
- Import then export with iFit:
  - sqw=iData_Sqw2D(‘file’)
  - sqw.saveas(‘file.sqw’,’mcstas’)
- Can/should always edit manually (text)
# weight 4.002 in [g/mol]
# density 0.4784 in [g/cm^3]
# sigma_abs 0.00747 absorption scattering cross section in [barn]
# sigma_coh 1.34 coherent scattering cross section in [barn]
# sigma_inc 0 incoherent scattering cross section in [barn]
# Temperature 2 in [K]
# classical 0 experimental, contains Bose factor

---
McStas: dyn from exp. DOS
- Import and correct data with e.g. LAMP, Mantid
- Estimate g(w) with e.g. LAMP, Mantid, MUPHOCOR
- Export to e.g. HDF/NeXus or other
- Import then export with iFit:
  - g=iData_vDOS(‘file’)
  - inc=g.incoherent;
  - inc.saveas(‘inc.sqw’,’mcstas’)
- Can/should always edit manually (text)

---
McStas: dyn from nuclear DB
- Import and export with iFit:
  - sqw=iData_Sqw2D(‘tsl.endf’)
  - saveas(sqw(1), ‘inc.sqw’,’mcstas’)
- Can/should always edit manually (text)
# weight 4.002 in [g/mol]
# density 0.4784 in [g/cm^3]
# sigma_abs 0.00747 absorption scattering cross section in [barn]
# sigma_coh 1.34 coherent scattering cross section in [barn]
# sigma_inc 0 incoherent scattering cross section in [barn]
# Temperature 2 in [K]
# classical 0 experimental, contains Bose factor

---
McStas: dyn from MD
- Import trajectory into MDANSE (converters)
- Double click the trajectory to allow analysis
- Use Plugins:
  - Analysis/Scattering/DCSF and DISF
  - Analysis/Scattering/Structure Factor
  - Analysis/Dynamics/Density of States
- Import then export with iFit:
  - sqw=iData_Sqw2D(‘DCSF.nc’)
  - sqw.saveas(‘coh.sqw’,’mcstas’)
- Can/should always edit manually (text)

---
McStas: dyn from nuclear DB
- Import and export with iFit:
  - sqw=iData_Sqw2D(‘tsl.endf’)
  - saveas(sqw(1), ‘inc.sqw’,’mcstas’)
- Can/should always edit manually (text)
# weight 4.002 in [g/mol]
# density 0.4784 in [g/cm^3]
# sigma_abs 0.00747 absorption scattering cross section in [barn]
# sigma_coh 1.34 coherent scattering cross section in [barn]
# sigma_inc 0 incoherent scattering cross section in [barn]
# Temperature 2 in [K]
# classical 0 experimental, contains Bose factor

---
McStas: dyn from Lattice Dynamics
- Using PhonoPy:
  - iFit: s4d=sqw_phonons(‘phonopy_directory’)
- Computing on the fly:
  - iFit: s4d=sqw_phonons(‘cod: La Mn O3’)
  - p=powder(s4d)
  - d=iData_Sqw2D(iData(p, [], 0:10, 0:100))
  - d.saveas(‘coh.sqw’,’mcstas’)
- Other:
  - Import in iFit, convert to Sqw2D, export.

---
Neutron events
- McStas handle ‘rays’ as packets of neutron events.
- Summing up builds intensity and distributions.
- McStas can read/write ‘events’ from other software:
  - MCNP TRAC and SSW
  - TRIPOLI
  - MCPL
- McStas can generate events as well for Mantid via NeXus/HDF files.

---
McStas automation: bash
- Can use cif2hkl and mcrun commands:
  - cif2hkl ‘file’ --out ‘file.laz’ --powder
  - mcrun –dir=test instr Powder=file.laz
  - mcplot.pl -psc test

---
McStas automation: iFit
iFit is a generic infrastructure which gathers data sets handling, fitting, S(q,w) models, and McStas hooks.

---
McStas iFit: build
- McStas can be controlled from within iFit.
- Open Matlab/iFit
- Create the McStas model with:
  - model = mccode(‘instr’)
- Plot the geometry with:
  - plot(model)	% has contextual menus
- Edit the instrument and re-compile
  - edit(model)

---
McStas iFit: eval
- Run with (default 1e6 event and pars)
  - data = iData(model, [], nan);
  - subplot(model) % plot monitors, contextual menus
- Specify parameters
  - data = iData(model, ‘lambda=2.36; coh=Cu.laz’)
- Do a scan:
  - data = iData(model, ‘lambda=[1.2 2.4 3.6]’)
- Change neutron events #
  - model.UserData.options.ncount = 1e7;

---
McStas iFit: optim
- Fix all parameters but lambda, Maximize model value:
  - mlock(model, ‘all’); munlock(model, ‘lambda’)
  - xlim(model, ‘lambda’, [1 3]); % bounds
  - fmax(model, ‘lambda=2.36’, ‘’, nan)
  - fmax(model, ‘lambda=2.36’, ‘OutputFcn=fminplot’, nan)

---
McStas iFit: advanced
- You can add McStas models:
  - model=mccode(‘instr1’)+mccode(‘instr2’) + ...
- For instance:
  - Instr1: structure
  - Instr2: spin-wave
  - Instr3: phonons
  - Instr4: incoherent
- The different models can also be assembled as a set of samples chosen at execution in a single McStas instrument.