## Slide 1
Sources and Monitors part 2.
Erik Knudsen, DTU Physics

## Slide 2
Sources: Source model overview
Reactors :
Source_Maxwell_3.comp
Source_gen.comp
Source_gen4.comp
Source_multi_surfaces.comp (*)
Mathematical:
  Source_simple.comp
  Source_div.comp
Pulsed sources:
  ESS_butterfly.comp
  ESS_moderator.comp
  Moderator.comp
  SNS_source.comp (*)
  SNS_source_analytic (*)
  ViewModISIS (*)
  ISIS_moderator.comp (*)
I/O mechanisms:
  MCPL_input/output.comp
  Virtual_input/output.comp
  Virtual_mcnp_ss_input/output.comp
  Virtual_tripoli4_input/output.comp
  Vitess_input/output.comp

## Slide 3
Sources: Source_Maxwell_3
Initial position and direction: as for Source_simple
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126, Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12, T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source

## Slide 4
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126, Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12, T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Intensity at a given wavelength drawn from a sum of (up to) 3 normalized Maxwellian distributions:
Parameters from the PSI cold source

## Slide 5
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126, Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12, T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source

## Slide 6
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126, Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12, T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Just for fun – let’s see what happens if we remove the fast peak…

## Slide 7
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126, Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12, T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Just for fun – let’s see what happens if we remove the fast peak…

## Slide 8
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126, Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12, T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

## Slide 9
COMPONENT vin = MCPL_input(filename=”voutput.mcpl”, polarisationuse=1,verbose=1)
AT (Xin,Yin,Zin) RELATIVE PREVIOUS
COMPONENT vout = MCPL_output(filename=”voutput.mcpl”, doubleprec=1,polarisationuse=1,verbose=1)
AT (Xout,Yout,Zout) RELATIVE PREVIOUS
Reads/writes events directly from MCPL-format files:
“T. Kittelmann et. al., “”, J. Phys. Comp., 2017
MCPL_input/output

## Slide 10
MCPL_input/output
MCPL_output.comp
n
n
n
(rx,ry,rz)0
(rx,ry,rz)1
(rx,ry,rz)2
AT(XOUT,YOUT,ZOUT)
Can include an Implicit Translation:

## Slide 11
MCPL_input.comp
n
n
n
(rx,ry,rz)0
(rx,ry,rz)1
(rx,ry,rz)2
AT(XIN,YIN,ZIN)
AT(XOUT,YOUT,ZOUT)
BECOMES
MCPL_output.comp
n
n
n
(rx,ry,rz)0
(rx,ry,rz)1
(rx,ry,rz)2
AT(XOUT,YOUT,ZOUT)
Can include an Implicit Translation:
MCPL_input/output

## Slide 12
Pulsed sources:
Simplest case:
Use a continuous source!
Model a source with given wavelength and spatial distribution
and
… an infinitely short pulse length. I.e. t = 0 for all neutron rays.
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin

## Slide 13
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin
EXTEND
%{
t=0;
%}
Pulsed sources:
Simplest case:
Use a continuous source!
Model a source with given wavelength and spatial distribution
and
… an infinitely short pulse length. I.e. t = 0 for all neutron rays.

## Slide 14
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin
EXTEND
%{
t=0;
%}
Pulsed sources:
Simplest case:
Use a continuous source!
Model a source with given wavelength and spatial distribution
and
… an infinitely short pulse length. I.e. t = 0 for all neutron rays.
Or: Use a chopper
(see later)

## Slide 15
Pulsed Sources: Moderator
A flat pulsed source with uniform energy spectrum:
Time structure is given by energy dependent probability density function:

## Slide 16
Pulsed Sources: ESS_butterfly
Analytic fits to MCNP-generated files.
Specialized fits to each beamport.
Fast and reasonably accurate.

## Slide 17
Pulsed Sources: ESS_butterfly

## Slide 18
Pulsed Sources: ESS_butterfly
"W" - 11

## Slide 19
Pulsed Sources: ESS_butterfly
"W" - 11

## Slide 20
Pulsed Sources: ESS_butterfly
"S" - 6

## Slide 21
Pulsed Sources: ESS_butterfly
Example: N-1

## Slide 22
Pulsed Sources: ESS_butterfly
n_pulses=3

## Slide 23
Pulsed Sources: ESS_butterfly
n_pulses=3

## Slide 24
Pulsed Sources: ViewModISIS
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Data file supplied for each beam port at ISIS.

## Slide 25
Pulsed Sources: ViewModISIS
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Data file supplied for each beam port at ISIS.
ISIS T2: IMAT

## Slide 26
Pulsed Sources: SNS_source
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Originally from SNS but also used extensively at J-PARC
Can be used (with the proper input files) to model CSNS, and likely also ISIS.

## Slide 27
Pulsed Sources: SNS_source
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Can be used (with the proper input files) to model CSNS-source.
Example (coming from you) is expected to be included in next release of McStas.

## Slide 28
Pulsed Sources: SNS_source_analytic
Samples from fits of Padé-functions to tallies from SNS_source.
- Requires a complex fitting campaign
+ Much faster than SNS_source + “Cleaner” distributions where statistics are sketchy
Can be used (with the proper input files) to model CSNS-source.

## Slide 29
Monitors (some)
1D
L_monitor →
TOF_monitor →
Hdiv_monitor →
MeanPolLambda →
E_monitor →
2D
PSD_monitor →
PSD_monitor_4PI →
PolLambda_monitor →
Divergence_monitor →
DivPos_monitor →
nD
Monitor_nD →
or
or
or ...

## Slide 30
Monitors: Quick examples
COMPONENT my_L_monitor = L_monitor(xwidth=0.2, yheight=0.2,
nL=20, filename="Output.L", Lmin=2, Lmax=10)

## Slide 31
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
In a histogram sense
…
…
In bin i, N events each carrying a fractional intensity pj so that
1
2
i
k
3

## Slide 32
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
In a histogram sense
…
…
In bin i, N events each carrying a fractional intensity pj so that
1
2
i
k
3
I
E
N
Monitors: Quick examples
Statistics computed on the fly
Intensity / n/s
Estimated RMS MC error
# Events
1st and 2nd moments of data

## Slide 33
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
In a histogram sense
…
…
In bin i, N events each carrying a fractional intensity pj so that
1
2
i
k
3
I
E
N
Monitors: Quick examples
Statistics computed on the fly
Intensity / n/s
Estimated RMS MC error
# Events
1st and 2nd moments of data
Statistics also available per bin (inside data file)

## Slide 34
Monitors: Quick examples
In 2D
1st and 2nd moments

## Slide 35
From "Virtual experiments - the ultimate aim of neutron ray-tracing simulations", K. Lefmann et al., Journal of Neutron Research 16, 97-111 (2008)

## Slide 36
From "Virtual experiments - the ultimate aim of neutron ray-tracing simulations", K. Lefmann et al., Journal of Neutron Research 16, 97-111 (2008)

## Slide 37
On a given McStas histogram
For the non-zero bins, calculate The smallest defines the “maximal counting time” allowed by your statistics
Preferably a “background” should be added - use a “known experimental value” or an estimate…
Sketch of an algorithm…

## Slide 38
Monitor_nD
A general monitor for 0D/1D/2D records
The all-in-one , swiss-army-knife of monitors
Monitor_nD can have almost any shape, and record
any requested standard quantities

## Slide 39
Monitor_nD
A general monitor for 0D/1D/2D records
COMPONENT MyMon = Monitor_nD( xwidth = 0.1, yheight = 0.1, zdepth = 0,
options = "intensity per cm2 angle,limits=[-5 5],
bins=10,with borders, file = mon1")
options = "banana, theta limits=[10,130], bins=120, y"
options = "multiple kx ky kz, auto abs log t, and list all neutrons"
Examples

## Slide 40
Monitor_nD
COMPONENT MyMon = Monitor_nD(xwidth = 0.1, yheight = 0.1,
user1=age, username1="Age of the Captain [years]",
options="user1, auto")
… or monitor just about anything:

## Slide 41
Exercise 2:
Head over to the github site and continue the exercise we started before:
https://github.com/McStasMcXtrace/Schools/tree/master/ISIS_April_2021/Tuesday_April_13th/2_Component_Basics/Exercise/